## Slide 1
디지털 시스템 및 마이크로컴퓨터 I
Digital System and Microcomputer I

## Slide 2: Digital System and Microcomputer I
교재
  Fundamentals of Logic Design (7th Ed.) by Charles H. Roth, Jr.
  http://airlab.inje.ac.kr
부교재
  Digital Fundamentals (10th Ed.) by Thomas L. Floyd
평가
  출석: 15%, 퀴즈: 25%, 중간고사: 30%, 기말고사: 30%

## Slide 3: 본 교과목을 왜 배워야 하는가?
Electronic Components
inside
Medical Equipment

## Slide 4: ECG: Electrocardiography

## Slide 5: Patient Monitor

## Slide 6: Infusion Pump

## Slide 7: Pulse Oximeter

## Slide 8: CT Scanner

## Slide 9: MRI: Magnetic Resonance Imaging

## Slide 10: X-Ray

## Slide 11: Ultrasound System

## Slide 12: Endoscope

## Slide 13: Digital Stethoscope

## Slide 14: Ventilator

## Slide 15: AED: Automated External Defibrillator

## Slide 16: Dialysis Machine

## Slide 17: EMG: Electromyography

## Slide 18: EEG: Electroencephalography

## Slide 19: For Disabled People

## Slide 20: Conclusion I
Microcontrollers and Digital Circuits
are
Key Components
in
Medical Equipment.

## Slide 21: What Else? - Industrial

## Slide 22: What Else? - Home Appliances

## Slide 23: What Else? - Entertainment

## Slide 24: Conclusion II
Microcontrollers
is
Everywhere.

## Slide 26: 의료기기의 설계 및 개발을 위한 필수 조건
사람 몸에 대한 이해
생체 신호에 대한 이해
전자회로에 대한 이해
디지털 시스템 및 컴퓨터에 대한 이해

## Slide 27
Computer Architecture
Digital System and Microcomputer I

## Slide 28: Computer Architecture
SOFTWARE
APPLICATION
OPERATING SYSTEM
FIRMWARE
HARDWARE

## Slide 29: Computer Software (1)
Program
  A set of instructions that the computer hardware can execute
Machine Instruction / Machine Language
  All programs are stored in the computer’s memory in the form of
  binary number (machine instruction)
  It is difficult and not productive.
Ex: Machine language program
  1001 0100 0001 0011b
    stands for “increment the contents of R1 register by 1.”
  0000 1100 0010 0001b
    stands for “add the contents of R1 register to the contents of R2 register.”

## Slide 30: Computer Software (2)
Assembly Language
  Invented to simplify the programming
  Consists of assembly instructions
  Mnemonic representation of a machine instruction
Ex: Assembly language program
  INC R1
  stands for “increment the contents of R1 register by 1.”
  ADD R2, R1
  stands for “add the contents of R1 register to the contents of R2 register.”

## Slide 31: Computer Architecture
SOFTWARE
APPLICATION
OPERATING SYSTEM
FIRMWARE
HARDWARE

## Slide 32: Computer Hardware
CPU
CONTROL
ALU
INPUT
OUTPUT
MEMORY
CPU: Central Processing Unit
ALU: Arithmetic Logic Unit

## Slide 33: Central Processing Unit (CPU)
CONTROL
UNIT
ALU
INSTRUCTION
REGISTER
PROGRAM COUNTER
STACK POINTER
REGISTER
FILE
TEMPORARY
REGISTERS

## Slide 34: Control Unit
CPU
CONTROL
INSTRUCTION
DECODER
CLOCK
INSTRUCTION
REGISTER
Control Signals
To Internal Registers
PROGRAM MEMORY
0000 1100 0010 0001b

## Slide 35: ALU, Register File, and Control Unit
CONTROL
INSTRUCTION
DECODER
CLOCK
INSTRUCTION
REGISTER
ALU
R1
R2
SREG
CPU
ADD R2,R1
PROGRAM MEMORY
0000 1100 0010 0001b

## Slide 36: Microprocessor (μP)
A processor(CPU) fabricated in a single IC
The number of bits of μP refers to
  the number of bits that μP can manipulate in one operation
Limitation of μP
  Requires external memory to execute programs.
  Cannot directly interface with I/O devices.
    Peripheral chips are needed.
  Address decoders and buffers are needed.
  Bigger system size

## Slide 37: Microprocessor-Based System
RWM
INPUT
OUTPUT
ROM
SYSTEM BUS
(Address, Data, Control)
μP

## Slide 38: Microcontroller
A computer implemented on a single VLSI chip
Contains everything a μP contains plus
  Memory
  Timer
  Analog-to-digital converter (ADC)
  Digital-to-analog converter (DAC)
  Parallel I/O interface
  Serial I/O interface
  Memory component interface circuitry

## Slide 39: General Microcontroller
PERIPHERALS
CONTROL
INSTRUCTION
DECODER
INSTRUCTION
REGISTER
ALU
R1
R2
SREG
CPU
ADD R2,R1

## Slide 40: Overview of 8-bit AVR Microcontroller
RISC architecture with CISC instruction set
  Powerful instruction set for C and Assembly
Scalable
  Same powerful AVR core in all devices
Single cycle execution
  One instruction per external clock
  Low power consumption
32 working Registers
  All directly connected to ALU!
Very efficient core
  20 MIPS @ 20MHz
High System Level Integration
  Lowest total system cost

## Slide 41
Introduction to 8-bit AVR Microcontroller

## Slide 42: ATmega328PB Features
Memories
  32 kBytes of In-System Self-Programmable Flash program memory
  1 kBytes EEPROM
  2 kBytes Internal SRAM
Peripherals
  Timer/Counters
  10-bit ADC
  USART
  SPI
  TWI
Operating Voltage: 1.8 - 5.5V
Speed Grade:
  0 - 4MHz @ 1.8 - 5.5V
  0 - 10MHz @ 2.7 - 5.5.V
  0 - 20MHz @ 4.5 - 5.5V

## Slide 43: ATmega328PB Block Diagram

## Slide 44: Summary
Number system
  Decimal, binary, and hexadecimal numbers
Computer organization
  hardware and software
Hardware
  CPU, input, output, and memory
Software
  Machine language, Assembly language
CPU
  ALU, register file, and control unit
Microprocessor
Microcontroller
AVR microcontroller

## Slide 46: 의료기기의 설계 및 개발을 위한 필수 조건
사람 몸에 대한 이해
생체 신호에 대한 이해
전자회로에 대한 이해
디지털 시스템 및 컴퓨터에 대한 이해

## Slide 47
컴퓨터 이해를 위한 필수 조건
디지털 시스템에 대한 이해

## Slide 48
What is Binary Digit?
Binary
  Two values (0, 1)
  Each digit is called as a “bit”
Number representation with only two values (0, 1)
Can be implemented with simple electronics devices
  examples:
    Voltage: HIGH(1), LOW(0)
    Switch: ON(1), OFF(0)
Good Things in Binary Number

## Slide 49: Number Systems
Decimal: 0..9
Binary: 0 and 1
Hexadecimal: 0..9 and A..F
Decimal | Binary | Hexadecimal
0 | 0 | 0
1 | 1 | 1
2 | 10 | 2
3 | 11 | 3
4 | 100 | 4
5 | 101 | 5
6 | 110 | 6
7 | 111 | 7
8 | 1000 | 8
9 | 1001 | 9
10 | 1010 | A
11 | 1011 | B
12 | 1100 | C
13 | 1101 | D
14 | 1110 | E
15 | 1111 | F
16 | 10000 | 10
17 | 10001 | 11

## Slide 50: Binary Arithmetic
Addition
Example:
0 + 0 = 0 | 
0 + 1 = 1 | 
1 + 0 = 1 | 
1 + 1 = 10 | (carry 1 to the next column)
 | 1 | 1 | 1 | 1 |  | ← carries
1310 = |  | 1 | 1 | 0 | 1 | 
1110 = |  | 1 | 0 | 1 | 1 | 
2410 = | 1 | 1 | 0 | 0 | 0 | 
+

## Slide 51: How to Implement an Adder (1)
Truth Table for a Half Adder
Half Adder
Half
Adder
0 0 | 0 0
0 1 | 0 1
1 0 | 0 1
1 1 | 1 0
0 0 | 0 0
0 1 | 0 1
1 0 | 0 1
1 1 | 1 0
X
Y
Cout
Sum
+
Exclusive OR
AND

## Slide 52: How to Implement an Adder (2)
Half Adder
Half
Adder
X
Y
Cout
Sum
+
Exclusive OR gate
AND gate

## Slide 53
Boolean Algebra
  Developed by George Boole
  Basic mathematics for logic design
  Restrict to switching circuits
    Two state values: 0, 1
    Switching algebra
Boolean Variable : X, Y, …
  Can only have two state values: 0, 1
  Representing True(1) or False (0)
Boolean Algebra

## Slide 54
Basic Operations of Boolean Algebra
  AND
  OR
  NOT
    Complement
    Inverse
Boolean Algebra

## Slide 55
Basic Operations (NOT)
NOT (Inverter)
Gate Symbol
1

## Slide 56
Basic Operations (AND)
A B | C = A · B
0 0 0 1 1 0 1 1 | 0 0 0 1
AND
Truth Table
Gate Symbol

## Slide 57
Basic Operations (OR)
A B | C = A + B
0 0 0 1 1 0 1 1 | 0 1 1 1
OR
Truth Table
Gate Symbol

## Slide 58
Hardware Architecture for Microcontroller
CONTROL
INSTRUCTION
DECODER
CLOCK
INSTRUCTION
REGISTER
ALU
R1
R2
SREG
CPU
ADD R2,R1
PROGRAM MEMORY
0000 1100 0010 0001b