## Slide 1
디지털시스템 및 마이크로 컴퓨터 I
10 주차 강의
Apr., 19, 2020
인제대학교 의용공학부
조 종만 교수

## Slide 2
Part 1 VHDL for Sequential Logic

## Slide 3
VHDL expression for F/F, shift register, counter
Sequential VHDL using process, if-else, case, wait..
Combination logic using process
VHDL: state machine
Compile, simulate, synthesize a circuit
Objectives

## Slide 4: VHDL Process
process structure
[process_name]: process (sensitivity_list)
begin
-- sequential statements.
end process;
(1) process_name: (선택사항) process의 이름
(2) sensitivity_list: (강제사항) 나열된 신호 중 하나라도 변하면 이 process가 실행됨.
(3) begin과 end 사이에 있는 sequential statements들은 순차적으로 수행된다.
(4) Process 안에 있는 signals들은 그 process 안의 모든 statements의 실행이 끝나야만 그 값들이 변한다.

## Slide 5: Sequential Statements
if-then-else statement
if condition then
sequential-statements
end if;
if condition1 then
sequential-statements1
elsif condition2 then
sequential-statements2
elsif condition3 then
sequential-statements3
else
sequential-statements4
end if;
if condition then
sequential-statements1
else
sequential-statements2
end if;

## Slide 6: Sequential Statements
case statement
case expression is
when choice1 => sequential statements1
when choice2 => sequential statements2
…
[when others => sequential statements]
end case;
If no action is specified for the other choices, the clause should be
when others => null;

## Slide 7: Modeling Flip-Flops Using VHDL Processes
VHDL Code for a Transparent Latch
library ieee;
use ieee.std_logic_1164.all;
entity t_latch is
port(D, G : in std_logic; -- data and clock inputs
Q : out std_logic); -- t_latch output
end t_latch ;
architecture prototype of t_latch is
begin
process(G, D)
begin
if G = ‘1’ then
Q <= D;
end if;
end process;
end prototype;
t_latch
simulation

## Slide 8: Modeling Flip-Flops Using VHDL Processes
VHDL Code for a Simple D Flip-Flop
library ieee;
use ieee.std_logic_1164.all;
entity d_ff is
port(D, CLK : in std_logic; -- data and clock inputs
Q : out std_logic); -- dff output
end d_ff ;
architecture prototype of d_ff is
begin
process (CLK)
begin
if (CLK’event and CLK=’1’) then
Q <= D;
end if; -- otherwise, does not change.
end process;
end prototype;
d_ff
simulation

## Slide 9: Modeling Flip-Flops Using VHDL Processes
VHDL Code For a D Flip-flop with Asynchronous Clear
library ieee;
use ieee.std_logic_1164.all;
entity d_ff is
port(D, CLK, ClrN : in std_logic;
Q : out std_logic);
end d_ff ;
architecture prototype of d_ff is
begin
process(CLK, ClrN)
begin
if ClrN = ‘0’ then
Q <= ‘0’;
elsif CLK’event and CLK=‘1’ then
Q <= D;
end if;
end process;
end prototype;
d_ff_clr
simulation

## Slide 10: Modeling Flip-Flops Using VHDL Processes
VHDL Code for a Simple D Flip-Flop (1)
library ieee;
use ieee.std_logic_1164.all;
entity d_ff_qn_1 is
port(D, CLK: in std_logic;
Q: buffer std_logic;
QN: out std_logic);
end entity;
architecture my_d_ff of d_ff_qn_1 is
begin
process(CLK)
begin
if (CLK'event and CLK='1') then
Q <= D;
QN <= not Q;
end if;
end process;
end architecture;
d_ff_qn_1
simulation
X

## Slide 11: Modeling Flip-Flops Using VHDL Processes
VHDL Code for a Simple D Flip-Flop (2)
library ieee;
use ieee.std_logic_1164.all;
entity d_ff_qn_1 is
port(D, CLK: in std_logic;
Q: buffer std_logic;
QN: out std_logic);
end entity;
architecture my_d_ff of d_ff_qn_1 is
begin
process(CLK)
begin
if (CLK'event and CLK='1') then
Q <= D;
end if;
end process;
QN <= not Q;
end architecture;
d_ff_qn_2
simulation
O

## Slide 12: Modeling Flip-Flops Using VHDL Processes
J-K Flip-Flop with Asynchronous Clear and Set
library ieee;
use ieee.std_logic_1164.all;
entity jk_ff is
port(SN, RN, J, K, CLK : in std_logic;
Q, QN : out std_logic);
end jk_ff ;
architecture prototype of jk_ff is
signal Qint: std_logic;
begin
Q <= Qint;
QN <= not Qint;
process(SN, RN, CLK)
begin
if RN = ‘0’ then Qint <= ‘0’;
elsif SN = ‘0’ then Qint <= ‘1’;
elsif CLK’event and CLK=‘1’ then
Qint <= (J and not Qint) or (not K and Qint);
end if;
end process;
end prototype;
jk_ff
simulation

## Slide 13
Part 2 VHDL for Sequential Logic

## Slide 14: Modeling Registers and Counters Using VHDL Processes
Register with Synchronous Clear and Load
library ieee;
use ieee.std_logic_1164.all;
entity sync_reg is
port(CLR, Ld, CLK: in std_logic;
D: in std_logic_vector(3 downto 0);
Q: out std_logic_vector(3 downto 0));
end entity;
architecture prototype of sync_reg is
begin
process(CLK)
begin
if CLK'event and CLK = '1' then
if CLR = '1' then Q <= "0000";
elsif Ld = '1' then Q <= D;
end if;
end if;
end process;
end architecture;
reg_syn_clr_ld
simulation

## Slide 15: Modeling Registers and Counters Using VHDL Processes
Left-Shift Register with Synchronous Clear and Load(1)
library ieee;
use ieee.std_logic_1164.all;
entity left_shift_reg is
port(Ld, LS, CLR, Rin, CLK: in std_logic;
D: in std_logic_vector(3 downto 0);
Q: buffer std_logic_vector(3 downto 0));
end entity;
architecture protytype of left_shift_reg is
begin
process(CLK)
begin
if (CLK'event and CLK='1') then
if (CLR='1') then Q <= "0000"; -- clear
elsif (Ld='1') then Q <= D; -- load
elsif (LS='1') then Q <= Q(2 downto 0) & Rin; -- shift left
end if;
end if;
end process;
end architecture;
left_shift_reg
simulation

## Slide 16: Modeling Registers and Counters Using VHDL Processes
Left-Shift Register with Synchronous Clear and Load(2)
library ieee;
use ieee.std_logic_1164.all;
entity left_shift_reg is
port(Ld, LS, CLR, Rin, CLK: in std_logic;
D: in std_logic_vector(3 downto 0);
Q: out std_logic_vector(3 downto 0));
end entity;
architecture protytype of left_shift_reg is
signal Qint: std_logic_vector(3 downto 0);
begin
process(CLK)
begin
if (CLK'event and CLK='1') then
if (CLR='1') then Qint <= "0000"; -- clear
elsif (Ld='1') then Qint <= D; -- load
elsif (LS='1') then Qint <= Qint(2 downto 0) & Rin; -- shift left
end if;
end if;
end process;
Q <= Qint;
end architecture;
left_shift_reg_1
simulation

## Slide 17: Modeling Registers and Counters Using VHDL Processes
VHDL Code for a Simple Synchronous Counter (1)
library ieee;
use ieee.std_logic_1164.all;
use ieee.std_logic_unsigned.all; -- needed for Q <= Q+1
entity counter is
port(ClrN, En, CLK: in std_logic;
Q: buffer std_logic_vector(3 downto 0));
end entity;
architecture prototype of counter is
begin
process(CLK)
begin
if CLK'event and CLK = '1' then
if ClrN = ‘0' then Q <= "0000";
elsif En = '1' then Q <= Q + 1; -- Q: buffer
end if;
end if;
end process;
end architecture;
simple_counter
simulation

## Slide 18: Modeling Registers and Counters Using VHDL Processes
VHDL Code for a Simple Synchronous Counter (2)
library ieee;
use ieee.std_logic_1164.all;
entity simple_counter_1 is
port(En, ClrN, CLK: in std_logic;
Q: out integer range 0 to 15);
end entity;
architecture counter of simple_counter_1 is
signal Qint: integer range 0 to 15;
begin
process(CLK)
begin
if (CLK'event and CLK='1') then
if (ClrN = '0') then Qint <= 0;
elsif (En='1') then Qint <= Qint + 1;
end if;
end if;
end process;
Q <= Qint;
end architecture;
simple_counter_1
simulation

## Slide 19: Modeling Registers and Counters Using VHDL Processes
Signal and Variable
 | SIGNAL | VARIABLE
할당 연산자 | <= | :=
활용 | 회로의 상호연결(전선)을 표현 | 지역적 정보를 표현
유효 범위 | 전역적 (코드 전체에서 볼 수 있음) | 지역적(해당 순차 코드 내부에서만 보임)
동작 | Sequential statement (예를 들면 process) 안에서 사용될 때, 이 신호의 값을 변경하는 문장을 사용하더라도 그 값의 변경은 즉각 이루어지지 않고 해당 statement가 종료된 후에 그 값이 갱신된다. | Sequential statement (예를 들면 process) 안에서 사용될 때, 이 변수의 값을 변경하는 문장을 사용하는 즉시 그 값의 변경이 이루어진다.
사용처 | package, entity, architecture에서 사용. entity에 있는 모든 port는 기본적으로 signal임 | Sequential statement 안에서만 사용

## Slide 20: Modeling Registers and Counters Using VHDL Processes
Signal and Variable: mod-10 counter (1)
library ieee;
use ieee.std_logic_1164.all;
entity mod_10_counter is
port( CLK: in std_logic;
count_out: out integer range 0 to 10);
end entity;
architecture my_counter of mod_10_counter is
signal count_int: integer range 0 to 10;
begin
mod_10_counter: process(CLK)
begin
if (CLK'event and CLK='1') then
count_int <= count_int + 1;
if (count_int = 10) then
count_int <= 0;
end if;
end if;
count_out <= count_int;
end process;
end architecture;
X

## Slide 21: Modeling Registers and Counters Using VHDL Processes
Signal and Variable: mod-10 counter (2)
library ieee;
use ieee.std_logic_1164.all;
entity mod_10_counter is
port( CLK: in std_logic;
count_out: out integer range 0 to 10);
end entity;
architecture my_counter of mod_10_counter is
signal count_int: integer range 0 to 10;
begin
mod_10_counter: process(CLK)
begin
if (CLK'event and CLK='1') then
count_int <= count_int + 1;
if (count_int = 9) then
count_int <= 0;
end if;
end if;
count_out <= count_int;
end process;
end architecture;

## Slide 22: Modeling Registers and Counters Using VHDL Processes
Signal and Variable: mod-10 counter (3)
library ieee;
use ieee.std_logic_1164.all;
entity mod_10_counter is
port( CLK: in std_logic;
count_out: out integer range 0 to 10);
end entity;
architecture my_counter of mod_10_counter is
begin
mod_10_counter: process(CLK)
variable count_int: integer range 0 to 10;
begin
if (CLK'event and CLK='1') then
count_int := count_int + 1;
if (count_int = 10) then
count_int := 0;
end if;
end if;
count_out <= count_int;
end process;
end architecture;

## Slide 23: Modeling Combination Logic Using VHDL Processes
VHDL Code for Gate Circuit
Every signal that appears on the right side of a signal assignment must appear on the sensitivity list.
library ieee;
use ieee.std_logic_1164.all;
entity gate_ckt is
port(A, B, D: in std_logic;
E: out std_logic);
end entity;
architecture prototype of gate_ckt is
signal C: std_logic;
begin
process(A, B, C, D)
begin
C <= A and B;
E <= C or D;
end process;
end architecture;

## Slide 24: Modeling Combination Logic Using VHDL Processes
case statement
case expression is
when choice1 => sequential statements1
when shoice2 => sequential statements2
…
[when others => sequential statements]
end case;
If no action is specified for the other choices, the clause should be
when other => null;

## Slide 25: Modeling Combination Logic Using VHDL Processes
Modeling of 4-to-1 MUX
library ieee;
use ieee.std_logic_1164.all;
entity mux_4_to_1 is
port(I0,I1,I2,I3,A,B: in std_logic;
F: out std_logic);
end entity;
architecture prototype of mux_4_to_1 is
signal sel: std_logic_vector(1 downto 0);
Begin
sel <= A & B;
process(sel, I0, I1, I2, I3)
begin
case sel is
when "00" => F <= I0;
when "01" => F <= I1;
when "10" => F <= I2;
when "11" => F <= I3;
when others => null;
end case;
end process;
end architecture;
when others => null;
This statement is required if sel is a std_logic_vector and omit if sel is a bit_vector
mux_4_to_1.vhd

## Slide 26: Modeling a State Machine
General Model of a Finite State Machine
process(reset, clock)
begin
if (reset=‘1’) then
present_state <= state0;
elsif (clock’event and clock=‘1’) then
present_state <= next_state;
end if;
end process;
VHDL template for the sequential circuit

## Slide 27: Modeling a State Machine
General Model of a Finite State Machine
process(input, present_state)
begin
case present_state is
when state0 =>
if (input = ...) then
output <= <value>;
next_state <= state1;
else ...
end if;
when state1 =>
if (input = ...) then
output <= <value>;
next_state <= state2;
else ...
end if;
when state2 =>
if (input = ...) then
output <= <value>;
next_state <= state3;
else ...
end if;
end case;
end process;
VHDL template for the combinational circuit

## Slide 28: Modeling a State Machine
Design of a Sequence Detector
Sequence
Detector
Clock
X
Z
하나의 입력 X와 하나의 출력 Z를 갖는 순차논리회로를 설계
연속해서 3개의 1이 입력 X에 공급될 때마다 출력 Z에 1이 출력됨.
중첩되는 1 입력 인정
x | 0 | 1 | 0 | 1 | 1 | 1 | 1 | 0 | 1
z | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 0 | 0
입출력 예
요구 사항

## Slide 29: Modeling a State Machine
Design of a Sequence Detector
Sequence
Detector
Clock
X
Z
State Graph

## Slide 30: Modeling a State Machine
Design of a Sequence Detector
library ieee;
use ieee.std_logic_1164.all;
entity fsm is
port(reset, clock, x: in std_logic;
z: out std_logic);
end entity;
architecture my_fsm of fsm is
type state is (S0, S1, S2, S3);
signal present_state, next_state: state;
begin
-- sequential circuit
process(reset, clock)
begin
if (reset='1') then
present_state <= S0;
elsif (clock'event and clock='1') then
present_state <= next_state;
end if;
end process;
-- combinational circuit
process(x, present_state)
begin
case present_state is
when S0 =>
z <= '0';
if (x = '1') then next_state <= S1;
else next_state <= S0;
end if;
when S1 =>
z <= '0';
if (x = '1') then next_state <= S2;
else next_state <= S0;
end if;
when S2 =>
z <= '0';
if (x = '1') then next_state <= S3;
else next_state <= S0;
end if;
when S3 =>
z <= '1';
if (x = '1') then next_state <= S3;
else next_state <= S0;
end if;
end case;
end process;
end architecture;
fsm
simulation