## Slide 1
디지털시스템 및 마이크로 컴퓨터 I
11 주차 강의
May 06, 2021
인제대학교 의용공학부
조 종만 교수

## Slide 2: Part 1 Introduction to Microcontroller

## Slide 3: Objectives
Computer Architecture
CPU, Microprocessor and Microcontroller
AVR Microcontrollers
ATmega328PB Microcontroller Registers

## Slide 4: Computer Organization
SOFTWARE
APPLICATION
OPERATING SYSTEM
FIRMWARE
HARDWARE

## Slide 5: Computer Hardware

## Slide 6: Computer Software (1)
Program
  A set of instructions that the computer hardware can execute
Machine Instruction / Machine Language
  All programs are stored in the computer’s memory in the form of binary number (machine instruction).
  It is difficult to use and not productive.
Ex: Machine language program
  1001 0100 0001 0011b
    stands for “increment the contents of R1 register by 1.”
  0000 1100 0010 0001b
    stands for “add the contents of R1 register to the contents of R2 register.”

## Slide 7: Computer Software (2)
Assembly Language
  Invented to simplify the programming
  Consists of assembly instructions
  Mnemonic representation of a machine instruction
Ex: Assembly language program
  INC R1
  stands for “increment the contents of R1 register by 1.”
  ADD R2, R1
  stands for “add the contents of R1 register to the contents of R2 register.”

## Slide 8: Central Processing Unit (CPU) (1)
Arithmetic Logic Unit (ALU)
  Execute numerical and logical operation
Register file
  Storage location inside the CPU
  Used to hold data / memory address
  Access to data in register is much faster than memory
  Number of registers varies depending on CPU
Control unit
  Hardware instruction logic
  Decodes and monitors the execution of instructions
  System clock synchronizes the activities of CPU

## Slide 9: Central Processing Unit (CPU) (2)
CONTROL
UNIT
ALU
INSTRUCTION
REGISTER
PROGRAM COUNTER
STACK POINTER
REGISTER
FILE
TEMPORARY
REGISTERS

## Slide 10: Control Unit
CPU
CONTROL
INSTRUCTION
DECODER
CLOCK
INSTRUCTION
REGISTER
Control Signals
To Internal Registers
PROGRAM MEMORY
0000 1100 0010 0001b

## Slide 11: ALU, Register File, and Control Unit
CONTROL
INSTRUCTION
DECODER
CLOCK
INSTRUCTION
REGISTER
ALU
R1
R2
SREG
CPU
ADD R2,R1
PROGRAM MEMORY
0000 1100 0010 0001b

## Slide 12: Microprocessor (μP)
A processor fabricated in a single IC
The number of bits of μP refers to
  the number of bits that μP can manipulate in one operation
Limitation of μP
  Requires external memory to execute programs.
  Cannot directly interface with I/O devices.
    Peripheral chips are needed.
  Address decoders and buffers are needed.
  Bigger system size

## Slide 13: Microprocessor-Based System (1)
RWM
INPUT
OUTPUT
ROM
SYSTEM BUS
(Address, Data, Control)
μP

## Slide 14: Microprocessor-Based System (2)
Dynalog, India에서 인용
Universidad Carlos IIIde Madris에서 인용
malinov.com에서 인용

## Slide 15: Memory Interface
Memory Interface Example (62256 - 32k x 8 bit Low Power CMOS Static RAM)
Memory
Microprocessor
Address Bus (A0~14)
Data Bus (I/O1~I/O8)
Control Bus (CS, WE, OE)

## Slide 16: Microcontroller
A computer implemented on a single VLSI chip
Contains everything a μP contains plus
  Memory
  Timer
  Analog-to-digital converter (ADC)
  Digital-to-analog converter (DAC)
  Parallel I/O interface
  Serial I/O interface
  Memory component interface circuitry
  Direct memory access (DMA)

## Slide 17: General Microcontroller
PERIPHERALS
CONTROL
INSTRUCTION
DECODER
INSTRUCTION
REGISTER
ALU
R1
R2
SREG
CPU
ADD R2,R1

## Slide 18: Part 2 Introduction to 8-bit AVR Microcontroller

## Slide 19: Overview of 8-bit AVR Microcontroller (1)
It is commonly accepted that AVR stands for Alf-Egil Bogen and Vegard Wollan's RISC processor.

## Slide 20: Overview of 8-bit AVR Microcontroller (2)
RISC architecture with CISC instruction set
  Powerful instruction set for C and Assembly
Scalable
  Same powerful AVR core in all devices
Single cycle execution
  One instruction per external clock
  Low power consumption
32 working Registers
  All directly connected to ALU!
Very efficient core
  20 MIPS @ 20MHz
High System Level Integration
  Lowest total system cost

## Slide 21: Overview of 8-bit AVR Microcontroller (3)
High Integration
Digital
AVR Core
Serial Interface
Analog
Non-volatile Memory

## Slide 22: Overview of 8-bit AVR Microcontroller (4)
Single Chip Solution

## Slide 23: Overview of 8-bit AVR Microcontroller (5)
Single Chip Solution

## Slide 24: Introduction to ATmega328PB

## Slide 25: ATmega328PB Features
Memories
  32 kBytes of In-System Self-Programmable Flash program memory
  1 kBytes EEPROM
  2 kBytes Internal SRAM
Peripherals
  Timer/Counters
  10-bit ADC
  USART
  SPI
  TWI
Operating Voltage: 1.8 - 5.5V
Speed Grade:
  0 - 4MHz @ 1.8 - 5.5V
  0 - 10MHz @ 2.7 - 5.5.V
  0 - 20MHz @ 4.5 - 5.5V

## Slide 26: ATmega328PB Block Diagram

## Slide 27: AVR CPU Core
AVR uses Harvard architecture
  Separate memories and buses for program and data
Single level pipelining for instruction (p.30)
Register File
  32 x 8-bit general purpose working registers with a single clock cycle access time
ALU (Arithmetic Logic Unit)
Status Register
  Contains information about the result of the most recently executed arithmetic instruction.
  This information can be used for altering program flow in order to perform conditional operations.
  The Status Register is updated after all ALU operations.
c.f. von Neuman architecture

## Slide 28: AVR Instruction Execution Timing (Pipeline)

## Slide 29: AVR Status Register
Bit No. | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
Name | I | T | H | S | V | N | Z | C
Reset | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Bit 7 – I: Global Interrupt Enable
Bit 6 – T: Copy Storage
Bit 5 – H: Half Carry Flag
Bit 4 – S: Sign Flag.
Bit 3 – V: Two’s Complement Overflow Flag
Bit 2 – N: Negative Flag
Bit 1 – Z: Zero Flag
Bit 0 – C: Carry Flag

## Slide 30: AVR General Purpose Register File
R0 | 0x00 | 
R1 | 0x01 | 
R2 | 0x02 | 
… |  | 
R13 | 0x0D | 
R14 | 0x0E | 
R15 | 0x0F | 
R16 | 0x10 | 
R17 | 0x11 | 
… |  | 
R26 | 0x1A | X-register Low Byte
R27 | 0x1B | X-register High Byte
R28 | 0x1C | Y-register Low Byte
R29 | 0x1D | Y-register High Byte
R30 | 0x1E | Z-register Low Byte
R31 | 0x1F | Z-register High Byte
Additional Function:
These registers are 16-bit address pointers for indirect addressing of the memory space.
X, Y, Z: for Data Memory
Z: Program Memory
Address
Bit 7 | Bit 6 | Bit 5 | Bit 4 | Bit 3 | Bit 2 | Bit 1 | Bit 0
Registers are special storages with 8 bits capacity.
They are connected directly to the CPU → fast access time.

## Slide 31: ATmega328PB Memories (1)
Two memory spaces of ATmega328PB
  Data memory
  Program memory
32 Registers | 0x0000-0x001F
64 I/O Registers | 0x0020-0x005F
160 Extended I/O Registers | 0x0060-0x00FF
Internal RAM (2048 x 8 bits) | 0x0100 0x08FF
Data Memory
Application Flash Section | 0x0000
Boot Flash Section | 0x3FFF
Program Memory

## Slide 32: ATmega328PB Memories (2)
In-System Reprogrammable Flash Program Memory
  Boot Loader Section
  Application Program Section
Application Flash Section | 0x0000
Boot Loader Section | 0x3FFF

## Slide 33: ATmega328PB Memories (3)
SRAM Data Memory Space
  Register File: 32
  I/O Registers: 64
  Extended I/O Registers: 160
  Internal data SRAM: 2048
32 Registers | 0x0000-0x001F
64 I/O Registers | 0x0020-0x005F
160 Extended I/O Registers | 0x0060-0x00FF
Internal RAM (2048 x 8 bits) | 0x0100 0x08FF

## Slide 34: Stack Pointer for AVR
Stack Pointer, SPL and SPH (0x3D and 0x3E)
  A stack is a last-in first-out data structure
  AVR stack is implemented as growing from higher to lower memory locations
  16-bit stack pointer(SPH:SPL) points to the top of stack (0x8FF)
32 Registers | 0x0000-0x001F
64 I/O Registers | 0x0020-0x005F
160 Extended I/O Registers | 0x0060-0x00FF
Internal RAM (2048 x 8 bits) | 0x0100 0x08FF
Data Memory

## Slide 35: Stack and Stack Pointer for AVR
1. LDI R16,0x08
2. OUT SPH,R16
3. LDI R16,0xFF
4. OUT SPL,R16
5. LDI R16,0x46
6. LDI R17,0x47
7. PUSH R16
8. PUSH R17
9. POP R17
10. POP R19
SPH:SPL
(0x08FF)
After Line #4
0x46
SPH:SPL
(0x08FE)
After Line #7
0x46
0x47
SPH:SPL
(0x08FD)
After Line #8
0x46
0x47
SPH:SPL
(0x08FE)
After Line #9
0x46
0x47
SPH:SPL
(0x08FF)
After Line #10
ATmega328PB RAM ADDRESS: 0x0100~0x08FF

## Slide 36: ATmega328PB Memories (4)
EEPROM Data Memory
  Electrically Erasable Programmable Read Only Memory
  1,024 Bytes of data EEPROM
  Can be accessible by byte unit.
  Endurance of at least 100,000 write/erase cycles.

## Slide 37
1. 교재
ATmega328PB 마이크로컨트롤러의 구조 및 프로그래밍
인제대학교 출판부, 조종만
ISBN: 978-89-6620-105-1
2. 부교재
ATmega328PB Website
(1) ATmega328PB Datasheet
Atmel corp.
(2) AVR Instruction Set Manual
Microchip Technology Inc.
(3) ATmega328PB Xplained Mini(Xmini)
(4) Atmel Studio 7
(Microchip 홈페이지에서 인용)

## Slide 38: Units for Memory Size
Specific units of IEC 60027-2 A.2 and ISO/IEC 80000
(International Electrotechnical Commission)
IEC prefix |  | Representations |  |  |  | Customary prefix | 
Name | Symbol | Base 2 | Base 1024 | Value | Base 10 | Name | Symbol
kibi | Ki | 210 | 10241 | 1024 | ≈1.02×10^3 | kilo | k, K
mebi | Mi | 220 | 10242 | 1,048,576 | ≈1.05×10^6 | mega | M
gibi | Gi | 230 | 10243 | 1,073,741,824 | ≈1.07×10^9 | giga | G
tebi | Ti | 240 | 10244 | 1,099,511,627,776 | ≈1.10×10^12 | tera | T
pebi | Pi | 250 | 10245 | 1,125,899,906,842,624 | ≈1.13×10^15 | peta | P
exbi | Ei | 260 | 10246 | 1,152,921,504,606,846,976 | ≈1.15×10^18 | exa | E
zebi | Zi | 270 | 10247 | 1,180,591,620,717,411,303,424 | ≈1.18×10^21 | zetta | Z
yobi | Yi | 280 | 10248 | 1,208,925,819,614,629,174,706,176 | ≈1.21×10^24 | yotta | Y

## Slide 39: Summary
Computer organization
  hardware and software
Hardware
  CPU, input, output, and memory
Software
  Machine language, Assembly language
CPU
  ALU, register file, and control unit
Microprocessor
Microcontroller
AVR microcontroller