## Slide 1
디지털시스템 및 마이크로 컴퓨터 I
12/13 주차 강의
Apr 20, 2022
인제대학교 의용공학부
조 종만 교수

## Slide 2: Objectives
Understanding ATmega328PB Instruction Set
  각 명령어의 기능/동작
  명령어 실행에 따른 SREG(Status Register)의 변화
  Opcode의 구성
  명령어 실행 시간
  데이터 메모리, 프로그램 메모리, 스택 메모리

## Slide 3: References
AVR Instruction Set Manual, DS40002198A, 2020
AVR Assembler (AVRASM2), DS40001917A, 2017
ATmega328PB Datasheet, DS40001906C, 2018

## Slide 4: Part 1 ATmega328PB Instruction Set (1)

## Slide 5: Assembly Language
High-Level Language
(C, C++, Pascal, Fortran)
Assembly Language
Machine Instruction
Hardware
x = 0x12;
y = 0x34;
z = x + y;
LDI R16,0x12
LDI R17,0x34
ADD R17,R16
MOV R24,R17
11100001 00000010
11100011 00010100
00001111 00010000
00101111 10000001
Compile
Assemble

## Slide 6: ATmega328PB Register File
R0 | 0x00
R1 | 0x01
R2 | 0x02
… | 
R13 | 0x0D
R14 | 0x0E
R15 | 0x0F
R16 | 0x10
R17 | 0x11
… | 
R26 | 0x1A
R27 | 0x1B
R28 | 0x1C
R29 | 0x1D
R30 | 0x1E
R31 | 0x1F
Data Memory Address
Bit 7 | Bit 6 | Bit 5 | Bit 4 | Bit 3 | Bit 2 | Bit 1 | Bit 0
ATmega328PB Registers are special storages with 8 bits capacity.
They are connected directly to the ALU → fast access time.
1 byte

## Slide 7: Assembly Language Statement Format
An assembly language statement line may take one of the four following forms:
  [label:] instruction [operands] [Comment]
  Comment
  Empty line
A comment has the following form:
  ; [Text]
Items placed in braces are optional.
The text between the comment-delimiter (;) and the end of line (EOL) is ignored by the Assembler.

## Slide 8: ATmega328PB Instruction Set(1)
The assembler is not case sensitive.
The operands have the following forms:
Rd: R0-R31 or R16-R31 (depending on instruction)
Rr: R0-R31
b: Constant (0-7), can be a constant expression
s: Constant (0-7), can be a constant expression
P: Constant (0-31/63), can be a constant expression
K: Constant (0-255), can be a constant expression
k: Constant, value range depending on instruction.
Can be a constant expression.
q: Constant (0-63), can be a constant expression

## Slide 9: 산술 논리 연산 명령어 (Instructions for Arithmetic and Logic Instructions)
ALU
R1
R2
SREG
CPU
ADD R2,R1

## Slide 10: ATmega328PB Instruction Set (2)
Mnemonics | Operands | Description | Operation | Flags | No. of Clock
ARITHMETIC AND LOGIC INSTRUCTIONS |  |  |  |  | 
ADD | Rd, Rr | Add without Carry | Rd ← Rd + Rr | Z,C,N,V,H | 1
ADC | Rd, Rr | Add with Carry | Rd ← Rd + Rr + C | Z,C,N,V,H | 1
ADIW | Rd, K | Add Immediate to Word | Rd+1:Rd ← Rd+1:Rd + K | Z,C,N,V | 2
SUB | Rd, Rr | Subtract without Carry | Rd ← Rd - Rr | Z,C,N,V,H | 1
SUBI | Rd, K | Subtract Immediate | Rd ← Rd - K | Z,C,N,V,H | 1
SBC | Rd, Rr | Subtract with Carry | Rd ← Rd - Rr - C | Z,C,N,V,H | 1
SBCI | Rd, K | Subtract Immediate with Carry | Rd ← Rd - K - C | Z,C,N,V,H | 1
SBIW | Rd, K | Subtract Immediate from Word | Rd+1:Rd ← Rd+1:Rd - K | Z,C,N,V | 2
AND | Rd, Rr | Logical AND | Rd ← Rd ∧ Rr | Z,N,V | 1
ANDI | Rd, K | Logical AND with Immediate | Rd ← Rd ∧ K | Z,N,V | 1
OR | Rd, Rr | Logical OR | Rd ← Rd ∨ Rr | Z,N,V | 1
ORI | Rd, K | Logical OR with Immediate | Rd ← Rd ∨ K | Z,N,V | 1

## Slide 11: ATmega328PB Instruction Set (3)
Mnemonics | Operands | Description | Operation | Flags | No. of Clock
ARITHMETIC AND LOGIC INSTRUCTIONS |  |  |  |  | 
COM | Rd | One's Complement | Rd ← $FF – Rd | Z,C,N,V | 1
NEG | Rd | Two's Complement | Rd ← $00 – Rd | Z,C,N,V,H | 1
SBR | Rd,K | Set Bit(s) in Register | Rd ← Rd ∨ K | Z,N,V | 1
CBR | Rd,K | Clear Bit(s) in Register | Rd ← Rd ∧ ($FFh - K) | Z,N,V | 1
INC | Rd | Increment | Rd ← Rd + 1 | Z,N,V | 1
DEC | Rd | Decrement | Rd ← Rd – 1 | Z,N,V | 1
TST | Rd | Test for Zero or Minus | Rd ← Rd ∧ Rd | Z,N,V | 1
CLR | Rd | Clear Register | Rd ← Rd Rd | Z,N,V | 1
SER | Rd | Set Register | Rd ← $FF | None | 1
MUL | Rd,Rr | Multiply Unsigned | R1, R0 ← Rd Rr | C | 2
Mnemonics | Operands | Description | Operation | Flags | No. of Clock
ARITHMETIC AND LOGIC INSTRUCTIONS |  |  |  |  | 
COM | Rd | One's Complement | Rd ← $FF – Rd | Z,C,N,V | 1
NEG | Rd | Two's Complement | Rd ← $00 – Rd | Z,C,N,V,H | 1
SBR | Rd,K | Set Bit(s) in Register | Rd ← Rd ∨ K | Z,N,V | 1
CBR | Rd,K | Clear Bit(s) in Register | Rd ← Rd ∧ ($FFh - K) | Z,N,V | 1
INC | Rd | Increment | Rd ← Rd + 1 | Z,N,V | 1
DEC | Rd | Decrement | Rd ← Rd – 1 | Z,N,V | 1
TST | Rd | Test for Zero or Minus | Rd ← Rd ∧ Rd | Z,N,V | 1
CLR | Rd | Clear Register |  | Z,N,V | 1
SER | Rd | Set Register | Rd ← $FF | None | 1
MUL | Rd,Rr | Multiply Unsigned |  | C | 2

## Slide 12
산술 연산 명령어
(Arithmetic Instructions)

## Slide 13: 수의 표현
unsigned 8-bit: 0부터 +255까지의 양수만을 표현
signed 8-bit: -128부터 +127까지의 수를 2의 보수 형태로 표현
8-비트의 2진수 표현 |  |  |  |  |  |  |  | unsigned | signed
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | +1 | +1
0 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | +127 | +127
1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | +128 | -128
1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | +255 | -1
ATmega328PB의 산술연산에서는 모두 signed 2’s complement 형식으로 취급

## Slide 14: Addition and Status Register (1)
8-비트 상수의 덧셈과 SREG
; 0x56+0x78=? (86+120=?)
LDI R16,0x56
LDI R17,0x78
ADD R16,R17
HERE: RJMP HERE
; 0x9A+0x78=? (-102+120=? )
LDI R16,0x9A
LDI R17,0x78
ADD R16,R17
HERE: RJMP HERE
 | carry |  |  | 0 |  | 1 | 1 | 1 | 0 |  | 0 | 0 | 0 | 
 | 0x56 |  |  |  |  | 0 | 1 | 0 | 1 |  | 0 | 1 | 1 | 0
+ | 0x78 |  | + |  |  | 0 | 1 | 1 | 1 |  | 1 | 0 | 0 | 0
 | 0xCE |  |  | 0 |  | 1 | 1 | 0 | 0 |  | 1 | 1 | 1 | 0
 | carry |  |  | 0 |  | 1 | 1 | 1 | 1 |  | 0 | 0 | 0 | 
 | 0x9A |  |  |  |  | 1 | 0 | 0 | 1 |  | 1 | 0 | 1 | 0
+ | 0x78 |  | + |  |  | 0 | 1 | 1 | 1 |  | 1 | 0 | 0 | 0
1 | 0x12 |  |  | 1 |  | 0 | 0 | 0 | 1 |  | 0 | 0 | 1 | 0

## Slide 15: AVR Status Register (SREG)
Bit No. | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
Name | I | T | H | S | V | N | Z | C
Reset | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Bit 7 – I: Global Interrupt Enable
Bit 6 – T: Copy Storage
Bit 5 – H: Half Carry Flag
Bit 4 – S: Sign Flag.
Can be used to determine if the result of a previous operation is positive or negative.
Bit 3 – V: Two’s Complement Overflow Flag
Bit 2 – N: Negative Flag. Same as bit 7 of previous operation.
Bit 1 – Z: Zero Flag
Bit 0 – C: Carry Flag

## Slide 16: Addition and Status Register (2)
16-비트 상수의 덧셈과 SREG
; 0x789A + 0x5679 = ? R19:R18 <- R19:R18 + R21:R20
; R19:R18 + R21:R20
;
LDI R18,0x9A ; Low Byte
LDI R19,0x78 ; High Byte
LDI R20,0x79 ; Low Byte
LDI R21,0x56 ; High Byte
ADD R18,R20 ; Add low byte first
ADC R19,R21 ; Add High byte with carry
HERE: RJMP HERE

## Slide 17: ATmega328PB Opcode (1)
ADD Rd,Rr
0000 | 11rd | dddd | rrrr
ADD R16,R17 d=16=10000, r=17=10001 opcode=0x0F01
0 ≤ d ≤ 31, 0 ≤ r ≤ 31
0000 | 1111 | 0000 | 0001
Assemble 후 생성된 list 파일(.lss) 참조
opcode: operation code
Register Direct

## Slide 18
논리 연산 명령어
(Logical Instructions)

## Slide 19: Logical Operation and Status Register
; 0xA5 ∧ 0x0F =?
LDI R16,0xA5
ANDI R16,0x0F
HERE: RJMP HERE
; 0xA5 0x0F = ?
LDI R16,0xA5
LDI R17,0x0F
EOR R16,R17
HERE: RJMP HERE
 | 0xA5 |  |  |  |  | 1 | 0 | 1 | 0 |  | 0 | 1 | 0 | 1
∧ | 0x0F |  | ∧ |  |  | 0 | 0 | 0 | 0 |  | 1 | 1 | 1 | 1
 | 0x05 |  |  | 0 |  | 0 | 0 | 0 | 0 |  | 0 | 1 | 0 | 1
 | 0xA5 |  |  |  |  | 1 | 0 | 1 | 0 |  | 0 | 1 | 0 | 1
 | 0x0F |  |  |  |  | 0 | 0 | 0 | 0 |  | 1 | 1 | 1 | 1
 | 0xAA |  |  | 0 |  | 1 | 0 | 1 | 0 |  | 1 | 0 | 1 | 0
 | 0xA5 |  |  |  |  | 1 | 0 | 1 | 0 |  | 0 | 1 | 0 | 1
 | 0x0F |  |  |  |  | 0 | 0 | 0 | 0 |  | 1 | 1 | 1 | 1
 | 0xAA |  |  | 0 |  | 1 | 0 | 1 | 0 |  | 1 | 0 | 1 | 0

## Slide 20: ATmega328PB Opcode (2)
Immediate Operand
ANDI Rd,K
0111 | KKKK | dddd | KKKK
ANDI R16,0x0F d=16-16=0=0000, K=0x0F=00001111 opcode=0x700F
16 ≤ d ≤ 31, 0 ≤ K ≤ 255
0111 | 0000 | 0000 | 1111
Assemble 후 생성된 list 파일(.lss) 참조

## Slide 21: Part 2 ATmega328PB Instruction Set (2)

## Slide 22
분기 명령어
(Branch Instructions)

## Slide 23: ATmega328PB Instruction Set (4)
Mnemonics | Operands | Description | Operation | Flags | No. of Clock
BRANCH INSTRUCTIONS |  |  |  |  | 
RJMP | k | Relative Jump | PC ← PC + k + 1 | None | 2
IJMP |  | Indirect Jump to (Z) | PC ← Z | None | 2
JMP | k | Jump | PC ← k | None | 3
RCALL | k | Relative Call Subroutine | PC ← PC + k + 1 | None | 3
ICALL |  | Indirect Call to (Z) | PC ← Z | None | 3
CALL | k | Call Subroutine | PC ← k | None | 4
RET |  | Subroutine Return | PC ← STACK | None | 4
RETI |  | Interrupt Return | PC ← STACK | I | 4
CPSE | Rd,Rr | Compare, Skip if Equal | if (Rd = Rr) PC ← PC + 2 or 3 | None | 1 / 2 / 3
CP | Rd,Rr | Compare | Rd - Rr | Z,C,N,V,H | 1
CPC | Rd,Rr | Compare with Carry | Rd - Rr - C | Z,C,N,V,H | 1
CPI | Rd,K | Compare with Immediate | Rd - K | Z,C,N,V,H | 1
SBRC | Rr, b | Skip if Bit in Register Cleared | if (Rr(b)=0) PC ← PC + 2 or 3 | None | 1 / 2 / 3
SBRS | Rr, b | Skip if Bit in Register Set | if (Rr(b)=1) PC ← PC + 2 or 3 | None | 1 / 2 / 3
SBIC | P, b | Skip if Bit in I/O Register Cleared | if(I/O(P,b)=0) PC ← PC + 2 or 3 | None | 1 / 2 / 3
SBIS | P, b | Skip if Bit in I/O Register Set | if(I/O(P,b)=1) PC ← PC + 2 or 3 | None | 1 / 2 / 3
BRBS | s, k | Branch if Status Flag Set | if (SREG(s) = 1) then PC ← PC + k + 1 | None | 1 / 2
BRBC | s, k | Branch if Status Flag Cleared | if (SREG(s) = 0) then PC ← PC + k + 1 | None | 1 / 2

## Slide 24: ATmega328PB Instruction Set (5)
Mnemonics | Operands | Description | Operation | Flags | No. of Clock
BRANCH INSTRUCTIONS |  |  |  |  | 
BREQ | k | Branch if Equal | if (Z = 1) then PC ← PC + k + 1 | None | 1 / 2
BRNE | k | Branch if Not Equal | if (Z = 0) then PC ← PC + k + 1 | None | 1 / 2
BRCS | k | Branch if Carry Set | if (C = 1) then PC ← PC + k + 1 | None | 1 / 2
BRCC | k | Branch if Carry Cleared | if (C = 0) then PC ← PC + k + 1 | None | 1 / 2
BRSH | k | Branch if Same or Higher | if (C = 0) then PC ← PC + k + 1 | None | 1 / 2
BRLO | k | Branch if Lower | if (C = 1) then PC ← PC + k + 1 | None | 1 / 2
BRMI | k | Branch if Minus | if (N = 1) then PC ← PC + k + 1 | None | 1 / 2
BRPL | k | Branch if Plus | if (N = 0) then PC ← PC + k + 1 | None | 1 / 2
BRGE | k | Branch if Greater or Equal, Signed | if (N V= 0) then PC ← PC+ k + 1 | None | 1 / 2
BRLT | k | Branch if Less Than, Signed | if (N V= 1) then PC ← PC + k + 1 | None | 1 / 2
BRHS | k | Branch if Half Carry Flag Set | if (H = 1) then PC ← PC + k + 1 | None | 1 / 2
BRHC | k | Branch if Half Carry Flag Cleared | if (H = 0) then PC ← PC + k + 1 | None | 1 / 2
BRTS | k | Branch if T Flag Set | if (T = 1) then PC ← PC + k + 1 | None | 1 / 2
BRTC | k | Branch if T Flag Cleared | if (T = 0) then PC ← PC + k + 1 | None | 1 / 2
BRVS | k | Branch if Overflow Flag is Set | if (V = 1) then PC ← PC + k + 1 | None | 1 / 2
BRVC | k | Branch if Overflow Flag is Cleared | if (V = 0) then PC ← PC + k + 1 | None | 1 / 2
BRIE | k | Branch if Interrupt Enabled | if (I = 1) then PC ← PC + k + 1 | None | 1 / 2
BRID | k | Branch if Interrupt Disabled | if (I = 0) then PC ← PC + k + 1 | None | 1 / 2
Mnemonics | Operands | Description | Operation | Flags | No. of Clock
BRANCH INSTRUCTIONS |  |  |  |  | 
BREQ | k | Branch if Equal | if (Z = 1) then PC ← PC + k + 1 | None | 1 / 2
BRNE | k | Branch if Not Equal | if (Z = 0) then PC ← PC + k + 1 | None | 1 / 2
BRCS | k | Branch if Carry Set | if (C = 1) then PC ← PC + k + 1 | None | 1 / 2
BRCC | k | Branch if Carry Cleared | if (C = 0) then PC ← PC + k + 1 | None | 1 / 2
BRSH | k | Branch if Same or Higher | if (C = 0) then PC ← PC + k + 1 | None | 1 / 2
BRLO | k | Branch if Lower | if (C = 1) then PC ← PC + k + 1 | None | 1 / 2
BRMI | k | Branch if Minus | if (N = 1) then PC ← PC + k + 1 | None | 1 / 2
BRPL | k | Branch if Plus | if (N = 0) then PC ← PC + k + 1 | None | 1 / 2
BRGE | k | Branch if Greater or Equal, Signed |  | None | 1 / 2
BRLT | k | Branch if Less Than, Signed |  | None | 1 / 2
BRHS | k | Branch if Half Carry Flag Set | if (H = 1) then PC ← PC + k + 1 | None | 1 / 2
BRHC | k | Branch if Half Carry Flag Cleared | if (H = 0) then PC ← PC + k + 1 | None | 1 / 2
BRTS | k | Branch if T Flag Set | if (T = 1) then PC ← PC + k + 1 | None | 1 / 2
BRTC | k | Branch if T Flag Cleared | if (T = 0) then PC ← PC + k + 1 | None | 1 / 2
BRVS | k | Branch if Overflow Flag is Set | if (V = 1) then PC ← PC + k + 1 | None | 1 / 2
BRVC | k | Branch if Overflow Flag is Cleared | if (V = 0) then PC ← PC + k + 1 | None | 1 / 2
BRIE | k | Branch if Interrupt Enabled | if (I = 1) then PC ← PC + k + 1 | None | 1 / 2
BRID | k | Branch if Interrupt Disabled | if (I = 0) then PC ← PC + k + 1 | None | 1 / 2

## Slide 25: 조건부 분기 명령어를 사용한 반복문
; 1부터 10까지의 합 구하기
sub r17,r17; sum=0, C=0
ldi r16,10; n=10
loop: add r17,r16
dec r16
brne loop
here: rjmp here
LDI, RJMP, ADC, SUB, DEC, BRNE

## Slide 26
데이터 이동 명령어
(Data Transfer Instructions)

## Slide 27: ATmega328PB Instruction Set (6)
Mnemonics | Operands | Description | Operation | Flags | No. of Clock
DATA TRANSFER INSTRUCTIONS |  |  |  |  | 
MOV | Rd, Rr | Copy Register | Rd ← Rr | None | 1
LDI | Rd, K | Load Immediate | Rd ← K | None | 1
LDS | Rd, k | Load Direct from SRAM | Rd ← (k) | None | 3
LD | Rd, X | Load Indirect | Rd ← (X) | None | 2
LD | Rd, X+ | Load Indirect and Post-Increment | Rd ← (X), X ← X + 1 | None | 2
LD | Rd, -X | Load Indirect and Pre-Decrement | X ← X - 1, Rd ← (X) | None | 2
LD | Rd, Y | Load Indirect | Rd ← (Y) | None | 2
LD | Rd, Y+ | Load Indirect and Post-Increment | Rd ← (Y), Y ← Y + 1 | None | 2
LD | Rd, -Y | Load Indirect and Pre-Decrement | Y ← Y - 1, Rd ← (Y) | None | 2
LDD | Rd,Y+q | Load Indirect with Displacement | Rd ← (Y + q) | None | 2
LD | Rd, Z | Load Indirect | Rd ← (Z) | None | 2
LD | Rd, Z+ | Load Indirect and Post-Increment | Rd ← (Z), Z ← Z+1 | None | 2
LD | Rd, -Z | Load Indirect and Pre-Decrement | Z ← Z - 1, Rd ← (Z) | None | 2
LDD | Rd, Z+q | Load Indirect with Displacement | Rd ← (Z + q) | None | 2
STS | k, Rr | Store Direct to SRAM | (k) ← Rr | None | 3
ST | X, Rr | Store Indirect | (X) ← Rr | None | 2

## Slide 28: ATmega328PB Instruction Set (7)
Mnemonics | Operands | Description | Operation | Flags | No. of Clock
DATA TRANSFER INSTRUCTIONS |  |  |  |  | 
ST | X+, Rr | Store Indirect and Post-Increment | (X) ← Rr, X ← X + 1 | None | 2
ST | -X, Rr | Store Indirect and Pre-Decrement | X ← X - 1, (X) ← Rr | None | 2
ST | Y, Rr | Store Indirect | (Y) ← Rr | None | 2
ST | Y+, Rr | Store Indirect and Post-Increment | (Y) ← Rr, Y ← Y + 1 | None | 2
ST | -Y, Rr | Store Indirect and Pre-Decrement | Y ← Y - 1, (Y) ← Rr | None | 2
STD | Y+q,Rr | Store Indirect with Displacement | (Y + q) ← Rr | None | 2
ST | Z, Rr | Store Indirect | (Z) ← Rr | None | 2
ST | Z+, Rr | Store Indirect and Post-Increment | (Z) ← Rr, Z ← Z + 1 | None | 2
ST | -Z, Rr | Store Indirect and Pre-Decrement | Z ← Z - 1, (Z) ← Rr | None | 2
STD | Z+q,Rr | Store Indirect with Displacement | (Z + q) ← Rr | None | 2
LPM |  | Load Program Memory | R0 ← (Z) | None | 3
IN | Rd, P | In Port | Rd ← P | None | 1
OUT | P, Rr | Out Port | P ← Rr | None | 1
PUSH | Rr | Push Register on Stack | STACK ← Rr | None | 2
POP | Rd | Pop Register from Stack | Rd ← STACK | None | 2

## Slide 29: ATmega328PB Data Memory Access
ATmega328PB의 데이터 메모리의 영역: 0-0x8FF
0000 0000 0000 0000 - 0000 1000 1111 1111
따라서 데이터 메모리를 access하기 위해서는 16 bits의 번지 지정 레지스터가 필요하다.
32 Registers | 0x0000-0x001F
64 I/O Registers | 0x0020-0x005F
160 Extended I/O Registers | 0x0060-0x00FF
Internal RAM (2048 x 8 bits) | 0x0100 0x08FF
1 byte
SP(Stack Pointer)
X-Register
Y-Register
Z-Register

## Slide 30: ATmega328PB Register File
R0 | 0x00 | 
R1 | 0x01 | 
R2 | 0x02 | 
… |  | 
R13 | 0x0D | 
R14 | 0x0E | 
R15 | 0x0F | 
R16 | 0x10 | 
R17 | 0x11 | 
… |  | 
R26 | 0x1A | X-register Low Byte
R27 | 0x1B | X-register High Byte
R28 | 0x1C | Y-register Low Byte
R29 | 0x1D | Y-register High Byte
R30 | 0x1E | Z-register Low Byte
R31 | 0x1F | Z-register High Byte
Additional Function:
These registers are 16-bit address pointers for indirect addressing of the memory space.
X, Y, Z: for Data Memory
Z: Program Memory
Address
Bit 7 | Bit 6 | Bit 5 | Bit 4 | Bit 3 | Bit 2 | Bit 1 | Bit 0
ATmega328PB Registers are special storages with 8 bits capacity.
They are connected directly to the CPU → fast access time.
1 byte

## Slide 31: 데이터 메모리 쓰기/읽기 (STS/LDS Instruction) (1)
; 데이터 메모리 0x102번지에 0x45를 저장
ldi r16,0x45
STS 0x102,R16
LDS R17,0x102
here: rjmp here
직접 번지 지정

## Slide 32: 데이터 메모리 쓰기/읽기 (ST/LD Instruction) (2)
; 데이터 메모리 0x102번지에 0x45를 저장
ldi r16,0x45
ldi XL,0x02 ; R26, low byte of address
ldi XH,0x01 ; R27, high byte of address
ST X,R16
LD R17,X
here: rjmp here
간접 번지 지정

## Slide 33: ATmega328PB Program Memory Access
Application Flash Section | 0x0000
Boot Loader Section | 0x3FFF
1 word (2 bytes)
ATmega328PB의 프로그램 메모리의 영역:
0000 0000 0000 0000 - 0011 1111 1111 1111
따라서 프로그램 메모리를 access하기 위해서는 16 bits의 번지 지정 레지스터가 필요하다.
PC(Program Counter), Z-Register
Program Counter (PC): 16 bits
word address

## Slide 34: Program Memory 읽기 (LPM Instruction)
; Program Memory의 TABLE 번지에 있는 내용을 읽어서 R17에 저장
;
ldi ZL,LOW(TABLE << 1) ; low byte of address
ldi ZH,HIGH(TABLE << 1) ; high byte of address
LPM R17,Z
here: rjmp here
;
; Program Memory의 TABLE 번지에 네 바이트의 상수를 저장
TABLE: .DB 0x41, 0x42, 0x43, 0x3A
List File (.lss) 읽는 방법

## Slide 35
비트 조작 명령어
(Bit and Bit Test Instructions)

## Slide 36: ATmega328PB Instruction Set (8)
Mnemonics | Operands | Description | Operation | Flags | No. of Clock
BIT AND BIT-TEST INSTRUCTIONS |  |  |  |  | 
LSL | Rd | Logical Shift Left | Rd(n+1) ← Rd(n), Rd(0) ← 0, C ← Rd(7) | Z,C,N,V,H | 1
LSR | Rd | Logical Shift Right | Rd(n) ← Rd(n+1), Rd(7) ← 0, C ← Rd(0) | Z,C,N,V | 1
ROL | Rd | Rotate Left Through Carry | Rd(0) ← C, Rd(n+1) ← Rd(n), C ← Rd(7) | Z,C,N,V,H | 1
ROR | Rd | Rotate Right Through Carry | Rd(7) ← C, Rd(n) ← Rd(n+1), C ← Rd(0) | Z,C,N,V | 1
ASR | Rd | Arithmetic Shift Right | Rd(n) ← Rd(n+1), n=0..6 | Z,C,N,V | 1
SWAP | Rd | Swap Nibbles | Rd(3..0) ↔ Rd(7..4) | None | 1
BSET | s | Flag Set | SREG(s) ← 1 | SREG(s) | 1
BCLR | s | Flag Clear | SREG(s) ← 0 | SREG(s) | 1
SBI | P, b | Set Bit in I/O Register | I/O(P, b) ← 1 | None | 2
CBI | P, b | Clear Bit in I/O Register | I/O(P, b) ← 0 | None | 2
BST | Rr, b | Bit Store from Register to T | T ← Rr(b) | T | 1
BLD | Rd, b | Bit load from T to Register | Rd(b) ← T | None | 1
SEC |  | Set Carry | C ← 1 | C | 1
CLC |  | Clear Carry | C ← 0 | C | 1
SEN |  | Set Negative Flag | N ← 1 | N | 1
CLN |  | Clear Negative Flag | N ← 0 | N | 1

## Slide 37: ATmega328PB Instruction Set (9)
Mnemonics | Operands | Description | Operation | Flags | No. of Clock
BIT AND BIT-TEST INSTRUCTIONS |  |  |  |  | 
SEZ |  | Set Zero Flag | Z ← 1 | Z | 1
CLZ |  | Clear Zero Flag | Z ← 0 | Z | 1
SEI |  | Global Interrupt Enable | I ← 1 | I | 1
CLI |  | Global Interrupt Disable | I ← 0 | I | 1
SES |  | Set Signed Test Flag | S ← 1 | S | 1
CLS |  | Clear Signed Test Flag | S ← 0 | S | 1
SEV |  | Set Two's Complement Overflow | V ← 1 | V | 1
CLV |  | Clear Two's Complement Overflow | V ← 0 | V | 1
SET |  | Set T in SREG | T ← 1 | T | 1
CLT |  | Clear T in SREG | T ← 0 | T | 1
SEH |  | Set Half Carry Flag in SREG | H ← 1 | H | 1
CLH |  | Clear Half Carry Flag in SREG | H ← 0 | H | 1
NOP |  | No Operation |  | None | 1
SLEEP |  | Sleep |  | None | 1
WDR |  | Watchdog Reset |  | None | 1

## Slide 38: I/O Register Control (SBI, CBI Instruction)
; PB5 핀에 펄스 신호를 출력
SBI DDRB,5
LOOP: SBI PORTB,5
NOP
CBI PORTB,5
NOP
RJMP LOOP
명령어 실행에 소요되는 Cycle 수 확인 방법

## Slide 39: Stack Memory and Stack Pointer for AVR
Stack Pointer, SPL and SPH (0x3D and 0x3E)
  A stack is a last-in first-out data structure
  AVR stack is implemented as growing from higher to lower memory locations
  16-bit stack pointer(SPH:SPL) points to the top of stack (0x8FF)
32 Registers | 0x0000-0x001F
64 I/O Registers | 0x0020-0x005F
160 Extended I/O Registers | 0x0060-0x00FF
Internal RAM (2048 x 8 bits) | 0x0100 0x08FF
Data Memory
Initial Stack Pointer

## Slide 40: Stack Pointer 초기화 및 PUSH/POP Instruction
1. LDI R16,0x08
2. OUT SPH,R16
3. LDI R16,0xFF
4. OUT SPL,R16
5. LDI R16,0x46
6. LDI R17,0x47
7. PUSH R16
8. PUSH R17
...
; R16, R17 사용
; R16, R17 내용변경
...
9. POP R17
10. POP R16
SPH:SPL
(0x08FF)
After Line #4
0x46
SPH:SPL
(0x08FE)
After Line #7
0x46
0x47
SPH:SPL
(0x08FD)
After Line #8
0x46
0x47
SPH:SPL
(0x08FE)
After Line #9
0x46
0x47
SPH:SPL
(0x08FF)
After Line #10
ATmega328PB RAM ADDRESS: 0x0100~0x08FF

## Slide 41: Subroutine 호출과 Stack Pointer (RCALL/RET Instruction)
; SP가 0x08FF로 초기화되어 있다고 가정
;
ldi r16,0x12
rcall mul2
here: rjmp here
;
mul2: add r16,r16
ret
SPH:SPL
(0x08FF)
초기 상태
1: 0000 e102 ldi r16,0x12
2: 0001 d001 rcall mul2
3: 0002 cfff here: rjmp here
;
4: 0003 0f00 mul2: add r16,r16
5: 0004 9508 ret
어셈블된 리스트 파일
02
00
SPH:SPL
(0x08FD)
2번행 실행 직후
4번행 실행 직전
02
00
SPH:SPL
(0x08FF)
5번행 실행 직후
3번행 실행 직전

## Slide 42: Summary
ATmega328PB Instruction Set
  각 명령어의 기능/동작
  명령어 실행에 따른 SREG(Status Register)의 변화
  Opcode의 구성
  명령어 실행 시간
  데이터 메모리, 프로그램 메모리, 스택 메모리
Assembly Language의 장점?

## Slide 43: What’s next?