## Slide 1
디지털시스템 및 마이크로 컴퓨터 I
14 주차 강의
Apr 20, 2022
인제대학교 의용공학부
조 종만 교수

## Slide 2: Objectives
ATmega328PB의 범용 입력 및 출력 관련 레지스터의 기능과 사용법
  범용입출력(general purpose input output, GPIO)이란?
  DDRx, PORTx, PINx 레지스터
  범용 출력
  범용 입력
  풀업 (pull-up) 저항
  범용 출력 핀의 전류 구동 능력

## Slide 3: References
ATmega328PB Datasheet, DS40001906C, 2018
AVR Instruction Set Manual, DS40002198A, 2020

## Slide 4: GPIO
(General Purpose Inputs Outputs)
Part 1

## Slide 5: GPIO (General Purpose Input Output)
General Purpose Input Output
    Is used for input or output binary data from/to a device whose communication protocol is not standard.
    Each port pin can be individually selectable for input or output mode.
    All port pins have individually selectable pull-up resistors with a supply-voltage invariant resistance.

## Slide 6: GPIO (General Purpose Input Output)
General Purpose Output is used
  to control a device whose function is controlled by binary value, i.e. ‘0’ or ‘1’.
  Examples: small dc power devices – Turn on/off LEDs

## Slide 7: GPIO (General Purpose Input Output)
General Purpose Output Example
  to control a device whose function is controlled by binary value, i.e. ‘0’ or ‘1’.
  Example: medium or high dc power devices - Turn on/off motors or lamps
Transistor
MOSFET

## Slide 8: GPIO (General Purpose Input Output)
General Purpose Output Example
  to control a device whose function is controlled by binary value, i.e. ‘0’ or ‘1’.
  Example: low to high DC or AC power devices – Turn on/off relays (heater, aircon)
Transistor
MOSFET

## Slide 9: GPIO (General Purpose Input Output)
General Purpose Input is used
  to accept signal from a device whose output is binary value, i.e. ‘0’ or ‘1’.
  Examples: switches
Switch

## Slide 10: GPIO (General Purpose Input Output)
General Purpose Input is used
  to accept signal from a device whose output is binary value, i.e. ‘0’ or ‘1’.
  Examples: opto-interrupter, rotary encoder
Rotary Encoder

## Slide 11: GPIO (General Purpose Input Output)
General Purpose Input is used
  to accept signal from a device whose output is binary value, i.e. ‘0’ or ‘1’.
  Examples: Hall-effect sensor, ultra-sonic sensor

## Slide 12: GPIO (General Purpose Input Output)
GPIO Registers
  DDRx register
    Data direction of GPIO pins
  PORTx register
    Output data value
  PINx register
    Input data value
x: Port name

## Slide 13: GPIO (General Purpose Input Output)
Example: Port B
  Bit 5 and 3: output
  Remaining bits: input
DDRx
x: Port name
DDRB, DDRC, DDRD
  Determines data direction of GPIO pins
    1 → Output
    0 → Input
Bit No. | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
Name | DDB7 | DDB6 | DDB5 | DDB4 | DDB3 | DDB2 | DDB1 | DDB0
Reset Value | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
DDRB = 0b00101000;
Bit No. | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
Name | DDB7 | DDB6 | DDB5 | DDB4 | DDB3 | DDB2 | DDB1 | DDB0
Value | 0 | 0 | 1 | 0 | 1 | 0 | 0 | 0
DDRB

## Slide 14: GPIO (General Purpose Input Output)
Example: Port B
  Bit 5: High, Bit 3: Low
  Remaining bits: input
PORTx
x: Port name
PORTB, PORTC, PORTD
  Holds output data value of GPIO pins
    1 → High (Vdd)
    0 → Low (GND)
Bit No. | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
Name | PORTB7 | PORTB6 | PORTB5 | PORTB4 | PORTB3 | PORTB2 | PORTB1 | PORTB0
Reset Value | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
PORTB = 0b00100000;
Bit No. | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
Name | PORTB7 | PORTB6 | PORTB5 | PORTB4 | PORTB3 | PORTB2 | PORTB1 | PORTB0
Value | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0
PORTB

## Slide 15: GPIO (General Purpose Input Output)
Example: Port B
  Turn on LEDs at PB6, PB4, PB3 and PB1
  Turn off LEDs at the remaining bits
PORTB = 0b01011010;
Bit No. | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
Name | PORTB7 | PORTB6 | PORTB5 | PORTB4 | PORTB3 | PORTB2 | PORTB1 | PORTB0
Value | 0 | 1 | 0 | 1 | 1 | 0 | 1 | 0

## Slide 16: GPIO (General Purpose Input Output)
PINx Registers
x: Port name
PINB, PINC, PIND
  Used to read input data value of GPIO pins
    High (Vdd) → 1
    Low (GND) → 0
Bit No. | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
Name | PINB7 | PINB6 | PINB5 | PINB4 | PINB3 | PINB2 | PINB1 | PINB0
Reset Value | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0

## Slide 17: GPIO (General Purpose Input Output)
Example: PINB register value
  Assume that all bits of Port B are input mode.
  PINB register value for the right-hand side circuit is
PINB == 0b10110110
Bit No. | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
Name | PINB7 | PINB6 | PINB5 | PINB4 | PINB3 | PINB2 | PINB1 | PINB0
Value | 1 | 0 | 1 | 1 | 0 | 1 | 1 | 0

## Slide 18: GPIO
(General Purpose Inputs Outputs)
Part 2

## Slide 19: GPIO (General Purpose Input Output)
Example: DDRB, PORTB and PINB registers
  Turn on LED at PB5 while a switch at PB7 is pressed (on).
#include <avr/io.h>
int main(void)
{
DDRB = 0b00100000; // set PB5 to OUTPUT mode
while (1)
{
if ((PINB & 0b10000000) == 0) // if switch at PB7 is pressed
PORTB = 0b00100000; // turn ON LED at PB5
else // else
PORTB = 0b00000000; // turn OFF LED at PB5
}
}

## Slide 20: GPIO (General Purpose Input Output)
Example: DDRB, PORTB and PINB registers
  Turn on LED at PB5 while a switch at PB7 is pressed (on).
#define SWITCH 7 // switch is connected at PB7
#define LED 5 // LED is connected at PB5
#include <avr/io.h>
int main(void)
{
DDRB |= 1 << LED; // set PB5 to OUTPUT mode
while (1)
{
if ((PINB & (1 << SWITCH)) == 0) // if switch at PB7 is pressed
PORTB |= 1 << LED; // turn ON LED at PB5
else // else
PORTB &= ~(1 << LED); // turn OFF LED at PB5
}
}

## Slide 21: GPIO (General Purpose Input Output)
Example: DDRB, PORTB and PINB registers
  Toggle LED at PB5 whenever a switch at PB7 is pressed.
// toggle by XOR with ‘1’
#include <avr/io.h>
int main(void)
{
DDRB |= (1 << 5); // set PB5 to OUTPUT mode
while (1)
{
if (!(PINB & (1 << 7))) // if switch at PB7 is pressed
{
PORTB ^= 1 << 5; // toggle LED at PB5
while (!(PINB & (1 << 7))); // wait until switch is released
}
}
}

## Slide 22: GPIO (General Purpose Input Output)
PINx Registers (used to toggle)
x: Port name
PINB, PINC, PIND
  Used to toggle data in the PORTx register
    Writing ‘1’ to PINxn → toggle n bit in the PORTx register
    Writing ‘0’ to PINxn → no change in the PORTx register

## Slide 23: GPIO (General Purpose Input Output)
Example: DDRB, PORTB and PINB registers
  Toggle LED at PB5 whenever a switch at PB7 is pressed.
// toggle by writing ‘1’ to PINB
#include <avr/io.h>
int main(void)
{
DDRB |= (1 << 5); // set PB5 to OUTPUT mode
while (1)
{
if (!(PINB & (1 << 7))) // if switch at PB7 is pressed
{
PINB |= 1 << 5; // toggle LED at PB5
while (!(PINB & (1 << 7))); // wait until switch is released
}
}
}

## Slide 24: GPIO (General Purpose Input Output)
Bit No. | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
Name | - | BODS | BODSE | PUD | - | - | IVSEL | IVCE
Reset Value | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
MCUCR
Global pull-up control: PUD bit in MCUCR register
    0 → Pull-up enable
    1 → All pull-ups in the GPIO are disabled.
Individual pull-up control: each bit in PORTx register for input mode
    1 → Pull-up enable
    0 → Pull-up in the GPIO pin is disabled.

## Slide 25: GPIO (General Purpose Input Output)
Example: DDRB, PORTB and PINB registers
  Turn on LED at PB5 while a switch at PB7 is pressed (on).
  External pull-up resistor was replaced by an internal pull-up resistor.
#include <avr/io.h>
int main(void)
{
DDRB = 0b00100000; // set PB5 to OUTPUT mode
PORTB = 0b10000000; // enable Pull-Up at PB7
while (1)
{
if ((PINB & 0b10000000) == 0) // if switch at PB7 is pressed
PORTB = 0b10100000; // turn ON LED at PB5
else // else
PORTB = 0b10000000; // turn OFF LED at PB5
}
}
atmega328p_gpio_input_output_internal_pull_up.png

## Slide 26: GPIO (General Purpose Input Output)
  Symmetrical drive characteristics with both high sink and source capability.
  IOH max = 20mA at VCC = 5V, 10mA at VCC = 3V
    The sum of all IOH, for ports C0 - C5, D0- D4, ADC7, RESET should not exceed 150mA.
    The sum of all IOH, for ports B0 - B5, D5 - D7, ADC6, XTAL1, XTAL2 should not exceed 150mA.
  IOL max = 20mA at VCC = 5V, 10mA at VCC = 3V
    The sum of all IOL, for ports C0 - C5, ADC7, ADC6 should not exceed 100mA.
    The sum of all IOL, for ports B0 - B5, D5 - D7, XTAL1, XTAL2 should not exceed 100mA.
    The sum of all IOL, for ports D0 - D4, RESET should not exceed 100mA.

## Slide 27: GPIO (General Purpose Input Output)
ATmega328P GPIO Pin Driver Strength

## Slide 28: What’s next?