## Slide 1
디지털시스템 및 마이크로 컴퓨터 I
2 주차 강의

## Slide 2
Part 1 Introduction to Number System and Conversion

## Slide 3
Objectives
Topics introduced in this chapter
Difference between analog and digital signal
Binary number and digital systems
Number systems and conversion
Add, subtract, multiply, divide positive binary numbers
1’s complement, 2’s complement for negative binary number
BCD code, 8-4-2-1 code, excess-3 code

## Slide 4: 1.1 Digital Systems
Digital systems: used in computation, data processing, control,
communication, measurement
- Accuracy, reliability: better than analog system
Analog – continuous
- Natural phenomena
(pressure, temperature, speed…)
- Difficulty in realizing, processing using electronics
Digital – discrete
- Binary digit → signal processing as bit unit
- Easy in realizing, processing using electronics
- High performance due to integrated circuit technology

## Slide 5: Analog (Continuous) vs Digital (Discrete) Signals
0
1
2
23
(time)
(temp.)
continuous
(time)
(temp.)
△ t
comparison
operation
recognition
※ △ t ≠ 0
discrete

## Slide 6: Analog (Continuous) vs Digital (Discrete) Signals
Digital signal
Discrete in amplitude
Discrete in time
Continuous in amplitude
Discrete in time
Sampled signal
amplitude
amplitude
Sampling
Quantization

## Slide 7
1.1 Binary Digit?
Binary: Two values (0, 1)
- Each digit is called as a “bit” (binary digit)
Number representation with only two values (0, 1)
Can be implemented with simple electronics devices
Ex: Voltage: HIGH(1), LOW(0)
Switch: ON(1), OFF(0)
Good Things in Binary Number

## Slide 8: 1.2 Number Systems and Conversion
Decimal: 0, 1, , 8, 9
Binary: 0 and 1
Hexadecimal: 0, 1, , 9 and A, , F
Decimal | Binary | Hexadecimal
0 | 0 | 0
1 | 1 | 1
2 | 10 | 2
3 | 11 | 3
4 | 100 | 4
5 | 101 | 5
6 | 110 | 6
7 | 111 | 7
8 | 1000 | 8
9 | 1001 | 9
10 | 1010 | A
11 | 1011 | B
12 | 1100 | C
13 | 1101 | D
14 | 1110 | E
15 | 1111 | F
16 | 10000 | 10
17 | 10001 | 11

## Slide 9: 1.2 Number Systems and Conversion
Decimal: uses digits from 0..9
Binary: uses only 0 and 1
Hexadecimal: uses digits from 0..9 and A..F
Positional Notation

## Slide 10: 1.2 Number Systems and Conversion
Radix(Base):
Example:
Positional Notation

## Slide 11: 1.2 Number Systems and Conversion
Conversion of decimal to base-R

## Slide 12: 1.2 Number Systems and Conversion
53
2
26
2
13
2
6
2
3
2
1
2
rem. = 1 = a0
rem. = 0 = a1
rem. = 1 = a2
rem. = 0 = a3
rem. = 1 = a4
0
rem. = 1 = a5
Example: decimal integer to binary conversion

## Slide 13: 1.2 Number Systems and Conversion
Conversion of a decimal fraction to base-R
Example:

## Slide 14: 1.2 Number Systems and Conversion
Conversion of binary to hexadecimal
10101111001001012 = ( )16
1001101.0101112 = 0100 1101.0101 11002 = 4D.5C16
11011010002 = ( )16

## Slide 15: 1.3 Binary Arithmetic
Addition
Example:
0 + 0 = 0 | 
0 + 1 = 1 | 
1 + 0 = 1 | 
1 + 1 = 0 | and carry 1 to the next column
 | 1 | 1 | 1 | 1 |  | carries
1310 = |  | 1 | 1 | 0 | 1 | 
1110 = |  | 1 | 0 | 1 | 1 | 
2410 = | 1 | 1 | 0 | 0 | 0 | 

## Slide 16: 1.3 Binary Arithmetic
note borrow from column 1
note borrow from column 2
Subtraction Example with Decimal

## Slide 17: 1.3 Binary Arithmetic
borrow
borrows
borrows
Subtraction
Example:
0 - 0 = 0 | 
0 - 1 = 1 | and borrow 1 from the next column
1 - 0 = 1 | 
1 - 1 = 0 | 

## Slide 18: 1.3 Binary Arithmetic
Multiplication
Multiply:
← multiplicand
← multiplier

## Slide 19: 1.3 Binary Arithmetic
Division
The quotient is with a remainder of .

## Slide 20: 1.4 Representation of Negative Numbers
Binary | Decimal
000 | 0
001 | 1
010 | 2
011 | 3
100 | 4
101 | 5
110 | 6
111 | 7
Zero and positive numbers only
(a) n-bit unsigned number
MSB |  |  |  | LSB
MSB |  |  |  | LSB
MSB: Most Significant Bit
LSB: Least Significant Bit
3-bit unsigned numbers

## Slide 21: 1.4 Representation of Negative Numbers
000 | 0
001 | 1
010 | 2
011 | 3
100 | -4
101 | -3
110 | -2
111 | -1
(b) n-bit signed number (2’s complement)
Zero, positive and negative numbers
Sign bit | Meaning
0 | Positive number ()
1 | Negative number ()
Sign bit | Meaning
0 | 
1 | 
MSB |  |  |  | LSB
MSB |  |  |  | LSB
3-bit signed number
(2’s complement)

## Slide 22: 1.4 Representation of Negative Numbers
4-bit representations for negative numbers
+N | Positive integers
+0 | 0000
+1 | 0001
+2 | 0010
+3 | 0011
+4 | 0100
+5 | 0101
+6 | 0110
+7 | 0111
- | -
-N | Negative integers |  | 
 | Sign and magnitude | 2’s complement | 1’s complement
-0 | 1000 | - | 1111
-1 | 1001 | 1111 | 1110
-2 | 1010 | 1110 | 1101
-3 | 1011 | 1101 | 1100
-4 | 1100 | 1100 | 1011
-5 | 1101 | 1011 | 1010
-6 | 1110 | 1010 | 1001
-7 | 1111 | 1001 | 1000
-8 | - | 1000 | -
-N | Negative integers |  | 
 | Sign and magnitude |  | 
-0 | 1000 | - | 1111
-1 | 1001 | 1111 | 1110
-2 | 1010 | 1110 | 1101
-3 | 1011 | 1101 | 1100
-4 | 1100 | 1100 | 1011
-5 | 1101 | 1011 | 1010
-6 | 1110 | 1010 | 1001
-7 | 1111 | 1001 | 1000
-8 | - | 1000 | -

## Slide 23: 1.4 Representation of Negative Numbers
1’s complement representation for the given number
Example: Find the 1’s complement of .

## Slide 24: 1.4 Representation of Negative Numbers
2’s complement representation for the given number
Example: Find the 2’s complement of .
2’s complement = 1’s complement + 1
방법1
방법2

## Slide 25: 1.4 Representation of Negative Numbers
Given a negative number by its 2’s complement,
 To obtain the magnitude of the integer
Taking 2’s complement of N*
2’s complement representation for the negative numbers
Example: 2의 보수 형태로 표시된 은 10진수 얼마에 해당하는가?
음수
-??
2의 보수

## Slide 26: 1.4 Representation of Negative Numbers
(correct answer)
wrong answer because of overflow (+1110 requires
5 bits including sign)
(correct answer)
Case 1
Case 2
Case 3
Addition of 2’s complement numbers
2의 보수를 취해서 더하면 뺄셈을 할 수 있음

## Slide 27: 1.4 Representation of Negative Numbers
correct answer when the carry from the sign bit
is ignored (this is not an overflow)
Case 4
Addition of 2’s complement numbers
Proof

## Slide 28: 1.4 Representation of Negative Numbers
correct answer when the last carry is ignored
(this is not an overflow)
Case 5
Addition of 2’s complement numbers
Proof

## Slide 29: 1.4 Representation of Negative Numbers
wrong answer because of overflow
(-1110 requires 5 bits including sign)
Case 6
Addition of 2’s complement numbers

## Slide 30: 1.5 Binary Codes
Decimal Digits | 8-4-2-1 Code (BCD) | Excess-3 Code | Gray Code
0 | 0000 | 0011 | 0000
1 | 0001 | 0100 | 0001
2 | 0010 | 0101 | 0011
3 | 0011 | 0110 | 0010
4 | 0100 | 0111 | 0110
5 | 0101 | 1000 | 1110
6 | 0110 | 1001 | 1010
7 | 0111 | 1010 | 1011
8 | 1000 | 1011 | 1001
9 | 1001 | 1100 | 1000
Gray code의 특징은?

## Slide 31: 1.5 Binary Codes
1010011 1110100 1100001 1110010 1110100
S t a r t
ASCII (American Standard Code for Information Interchange) Code

## Slide 32
ASCII Code (incomplete)

## Slide 33
Part 1 Summary
Topics introduced in this chapter
Difference between analog and digital signal
Binary number and digital systems
Number systems and conversion
Add, subtract, multiply, divide positive binary numbers
1’s complement, 2’s complement for negative binary number
BCD code, 8-4-2-1 code, excess-3 code

## Slide 34
Summary
Topics introduced in this chapter
Difference between Analog and Digital signal
Difference between Combinational and Sequential Circuits
Binary number and digital systems
Number systems and Conversion
Add, Subtract, Multiply, Divide Positive Binary Numbers
1’s Complement, 2’s Complement for Negative binary number
BCD code, excess-3 code, gray code

## Slide 35
Week 2 - Part 2 Boolean Algebra

## Slide 36
Objectives
Topics introduced in this chapter:
Understand the basic operations and laws of Boolean algebra
Relate these operations and laws to AND, OR, NOT gates and switches
Prove these laws using a truth table
Manipulation of algebraic expression using
  - Multiplying out
  - Factoring
  - Simplifying
  - Finding the complement of an expression
XOR, XNOR, NAND, NOR

## Slide 37
2.1 Introduction
Boolean Algebra
  Developed by George Boole
  Basic mathematics for logic design
  Restrict to switching circuits
    Two state values: 0, 1
    Switching algebra
Boolean Variable : X, Y, …
  Can only have two state values: 0, 1
  Representing True(1) or False (0)

## Slide 38
2.2 Basic Operations
Basic Operations of Boolean Algebra
  AND
  OR
  NOT (Complement, Inverse)
Logic Gate
    Electronic device implementing a Boolean function or a logical operation

## Slide 39
2.2 Basic Operations (NOT)
A | Q = A’
0 1 | 1 0
Truth Table
Gate Symbol

## Slide 40
2.2 Basic Operations (AND)
A B | Q = A·B
0 0 0 1 1 0 1 1 | 0 0 0 1
Truth Table
Gate Symbol

## Slide 41
2.2 Basic Operations (OR)
A B | Q = A + B
0 0 0 1 1 0 1 1 | 0 1 1 1
Truth Table
Gate Symbol

## Slide 42
2.2 Basic Operations
Apply to Switch
AND
OR

## Slide 43
2.3 Boolean Expressions and Truth Tables
Boolean Expression
  Consists of the basic operations to one or more Boolean variables or constants
  Precedence
    Parentheses ()
    NOT
    AND
    OR
Example

## Slide 44
2.3 Boolean Expressions and Truth Tables
Boolean Expression
Logic Circuit for Boolean Expression

## Slide 45
2.3 Boolean Expressions and Truth Tables
Boolean Expression
Logic Circuit for Boolean Expression

## Slide 46
2.3 Boolean Expressions and Truth Tables
Literal
  Each appearance of a variable or its complement in a Boolean expression
  Example
  Corresponds to a gate input
10 literals
Evaluation of Boolean Expression
  By substituting a value 0 or 1 for each variable
Example
Evaluate when
Answer:

## Slide 47
2.3 Boolean Expressions and Truth Tables
A B | A’ | F = A’ + B
0 0 0 1 1 0 1 1 | 1 1 0 0 | 1 1 0 1
Truth Table
  Specifies the value of a Boolean expression for every possible combination of value of the variables in the expression
  Specifies the output values for a circuit logic gates in terms of the values of the input variables
Example: 2-input logic circuit

## Slide 48: Proof an equation using truth table
2.3 Boolean Expressions and Truth Tables
A B C | B’ | AB’ | AB’ + C | A + C | B’ + C | (A + C) (B’ + C)
0 0 0 0 0 1 0 1 0 0 1 1 1 0 0 1 0 1 1 1 0 1 1 1 | 1 1 0 0 1 1 0 0 | 0 0 0 0 1 1 0 0 | 0 1 0 1 1 1 0 1 | 0 1 0 1 1 1 1 1 | 1 1 0 1 1 1 0 1 | 0 1 0 1 1 1 0 1
Truth table
n variable needs rows.
n times

## Slide 49: 2.4 Basic Theorems
Example
Operations with 0, 1
Idempotent Laws
Involution Laws
Complementary Laws
Idempotent law 멱등법칙(冪等法則) 또는 멱등성(冪等性): 연산을 여러 번 적용하더라도 결과가 달라지지 않는 성질

## Slide 50: 2.4 Basic Theorems with Switch Circuits
Equivalent Switch Circuits

## Slide 51: 2.4 Basic Theorems with Switch Circuits
Equivalent Switch Circuits

## Slide 52: 2.4 Basic Theorems with Switch Circuits
Equivalent Switch Circuits

## Slide 53: 2.4 Basic Theorems with Switch Circuits
Equivalent Switch Circuits

## Slide 54: 2.5 Commutative, Associative, and Distributive Laws
Commutative Laws:
Associative Laws:
X Y Z | XY YZ | (XY)Z X(YZ)
0 0 0 | 0 0 | 0 0
0 0 1 | 0 0 | 0 0
0 1 0 | 0 0 | 0 0
0 1 1 | 0 1 | 0 0
1 0 0 | 0 0 | 0 0
1 0 1 | 0 0 | 0 0
1 1 0 | 1 0 | 0 0
1 1 1 | 1 1 | 1 1
Proof of Associative Law for AND

## Slide 55
Associative Laws for AND and OR
Associative Law Using AND Gates
0
Associative Law Using OR Gates

## Slide 56: Distributive Laws
Distributive Laws:
Valid only Boolean algebra not for ordinary algebra
Proof

## Slide 57: 2.6 Simplification Theorems
Useful Theorems for Simplification
Proof
Why Simplify?
Simplifying the corresponding logic circuit

## Slide 58: Application of Simplification Theorem to Equivalent Gate Circuits
2.6 Simplification Theorems

## Slide 59
2.6 Simplification Theorems
Example 1: Simplify
Solution:

## Slide 60
2.6 Simplification Theorems
Example 2:
Simplify
Solution:

## Slide 61: 2.7 Multiplying Out and Factoring
Multiplying out using distributive laws can obtain a
sum-of-products (SOP) form
Sum-of-product form:
Not in Sum-of-product form

## Slide 62: 2.7 Multiplying Out and Factoring
Example: Multiply out
(Solution 1)
← Non SOP form
← SOP form
(Solution 2)
← SOP form

## Slide 63: 2.7 Multiplying Out and Factoring
Product-of-sum form
Factoring using distributive laws can obtain a
product-of-sums (POS) form

## Slide 64: 2.7 Multiplying Out and Factoring
Example1: Factor A+B’CD
(Solution)
← Non POS form
← POS form

## Slide 65: Circuits for Sum-of-Products Form
AB′ + CD′E + AC′E′
A + B′ + C + D′E
AND
OR
AND
OR

## Slide 66: Circuits for Product-of-Sums Form
(A +B′)(C + D′ + E)(A + C′ + E′)
AND
OR
AND
OR
AB′C(D′ + E)

## Slide 67: 2.8 DeMorgan’s Laws
X Y | X’ Y’ | X + Y | ( X + Y )’ | X’ Y’ | XY | ( XY )’ | X’ + Y’
0 0 0 1 1 0 1 1 | 1 1 1 0 0 1 0 0 | 0 1 1 1 | 1 0 0 0 | 1 0 0 0 | 0 0 0 1 | 1 1 1 0 | 1 1 1 0
DeMorgan’s Laws
Proof

## Slide 68: 2.8 DeMorgan’s Laws
DeMorgan’s Laws for n variables
Example: Find the complement of .

## Slide 69: 2.8 DeMorgan’s Laws
A B | A’ B | A B’ | F = A’B+AB’ | A’ B’ | A B | F’ = A’B’ + AB
0 0 0 1 1 0 1 1 | 0 1 0 0 | 0 0 1 0 | 0 1 1 0 | 1 0 0 0 | 0 0 0 1 | 1 0 0 1
Complement of
← XOR
← XNOR, EQUIVALENT

## Slide 70: 2.9 Exclusive-OR and Equivalence Operations
Exclusive-OR
XOR
Truth Table
Symbol
Equation
X Y | XY
0 0 0 1 0 1 1 | 0 1 1 0
X Y | 
0 0 0 1 0 1 1 | 0 1 1 0

## Slide 71: 2.9 Exclusive-OR and Equivalence Operations
Theorems for Exclusive-OR
(Equivalence)

## Slide 72
Equivalence operation
(Exclusive-NOR, XNOR)
Truth Table
Symbol
Equation
2.9 Exclusive-OR and Equivalence Operations
X Y | XY
0 0 0 1 0 1 1 | 1 0 0 1
X Y | 
0 0 0 1 0 1 1 | 1 0 0 1

## Slide 73: 2.10 NAND and NOR Gates
NAND gate

## Slide 74: 2.10 NAND and NOR Gates
NOR gate

## Slide 75: 2.10 NAND and NOR Gates
OR realized by using AND and NOT gates

## Slide 76: 2.10 NAND and NOR Gates
NAND gate realization of NOT, AND and OR gates
AND realized by using OR and NOT

## Slide 77
Part 2 Summary
Topics introduced in this chapter:
Understand the basic operations and laws of Boolean algebra
Relate these operations and laws to AND, OR, NOT gates and switches
Prove these laws using a truth table
Manipulation of algebraic expression using
  - Multiplying out
  - Factoring
  - Simplifying
  - Finding the complement of an expression
XOR, XNOR, NAND, NOR