## Slide 1
디지털시스템 및 마이크로 컴퓨터 I
3 주차 강의
Mar., 26 2020

## Slide 2
Part 1 Applications of Boolean Algebra/ Minterm and Maxterm Expansions

## Slide 3
Conversion of Verbal Description to Boolean Equations
Combinational Logic Design Using a Truth Table
Minterm and Maxterm Expansions
Incompletely Specified Functions (Don’t care term)
Design of Binary Adders(Full adder) and Subtractors
Objective

## Slide 4: 3.1 Conversion of Verbal Description to Boolean Equations
Steps in designing a single-output combinational switching circuit
Find a switching function which specifies the desired behavior of the circuit
Find a simplified algebraic expression for the function
Realize the simplified function using available logic elements

## Slide 5: 3.1 Conversion of Verbal Description to Boolean Equations
Mary watches TV if it is Monday night and she has finished her homework.
F is ‘true’ if A and B are both ‘true’  F = A·B
Example 1
F = 1 if “Mary watches TV ” is true; otherwise, F = 0;
A = 1 if “it is Monday night ” is true; otherwise, A = 0;
B = 1 if “she has finished her homework” is true; otherwise, B = 0;
Verbal Description

## Slide 6
The alarm will ring iff the alarm switch is turned on and the door is not closed, or it is after 6PM and window is not closed.
The alarm will ring iff
the alarm switch is turned on and the door is not closed,
or it is after 6PM and window is not closed.
Z
A
B’
C
D’
Breaking Down
3.1 Conversion of Verbal Description to Boolean Equations
Example 2
Verbal Description

## Slide 7
Boolean Equation
3.1 Conversion of Verbal Description to Boolean Equations
The alarm will ring iff
the alarm switch is turned on and the door is not closed,
or it is after 6PM and window is not closed.
Z
A
B’
C
D’
Verbal Description

## Slide 8
Circuit Realization
3.1 Conversion of Verbal Description to Boolean Equations
Boolean Equation

## Slide 9
3.2 Combinational Logic Design Using a Truth Table
A switching circuit with three inputs and one output.
The inputs are A, B, and C and represent a binary number N.
f = 1 if N ≥ 0112 and f = 0 if N < 0112
Verbal Description

## Slide 10
3.2 Combinational Logic Design Using a Truth Table
A switching circuit with three inputs and one output.
The inputs are A, B, and C and represent a binary number N.
f = 1 if N ≥ 0112 and f = 0 if N < 0112
Verbal Description
A B C | f
0 0 0 | 0
0 0 1 | 0
0 1 0 | 0
0 1 1 | 1
1 0 0 | 1
1 0 1 | 1
1 1 0 | 1
1 1 1 | 1

## Slide 11
Deriving an algebraic expression for f = 1
Simplifying the algebraic expression
A B C | f
0 0 0 | 0
0 0 1 | 0
0 1 0 | 0
0 1 1 | 1
1 0 0 | 1
1 0 1 | 1
1 1 0 | 1
1 1 1 | 1
3.2 Combinational Logic Design Using a Truth Table

## Slide 12
Simplified Equation
Circuit Realization
Original Equation
3.2 Combinational Logic Design Using a Truth Table

## Slide 13
Expression for f = 0 i.e. f’ = 1
Taking the complement of f ’
3.2 Combinational Logic Design Using a Truth Table
A B C | f | f’
0 0 0 | 0 | 1
0 0 1 | 0 | 1
0 1 0 | 0 | 1
0 1 1 | 1 | 0
1 0 0 | 1 | 0
1 0 1 | 1 | 0
1 1 0 | 1 | 0
1 1 1 | 1 | 0

## Slide 14
3.2 Combinational Logic Design Using a Truth Table
Expression for f = 0
A B C | f | f’
0 0 0 | 0 | 1
0 0 1 | 0 | 1
0 1 0 | 0 | 1
0 1 1 | 1 | 0
1 0 0 | 1 | 0
1 0 1 | 1 | 0
1 1 0 | 1 | 0
1 1 1 | 1 | 0

## Slide 15
Simplifying
3.2 Combinational Logic Design Using a Truth Table
A B C | f | f’
0 0 0 | 0 | 1
0 0 1 | 0 | 1
0 1 0 | 0 | 1
0 1 1 | 1 | 0
1 0 0 | 1 | 0
1 0 1 | 1 | 0
1 1 0 | 1 | 0
1 1 1 | 1 | 0

## Slide 16: 3.3 Minterm and Maxterm Expansions
Literal
A variable or its complement (e.g. A, A’)
Minterm of n variables
A product of n literals in which each variable appears exactly once in either true or complemented form, but not both
Notation
mi

## Slide 17: 3.3 Minterm and Maxterm Expansions
Row No. | A B C | Minterms | Maxterms
0 1 2 3 4 5 6 7 | 0 0 0 0 0 1 0 1 0 0 1 1 1 0 0 1 0 1 1 1 0 1 1 1 |  | A+B+C = M0 A+B+C’ = M1 A+B’+C = M2 A+B’+C’ = M3 A’+B+C = M4 A’+B+C’ = M5 A’+B’+C = M6 A’+B’+C’ = M7
Row No. | A B C | Minterms | Maxterms
0 1 2 3 4 5 6 7 | 0 0 0 0 0 1 0 1 0 0 1 1 1 0 0 1 0 1 1 1 0 1 1 1 |  | A+B+C = M0 A+B+C’ = M1 A+B’+C = M2 A+B’+C’ = M3 A’+B+C = M4 A’+B+C’ = M5 A’+B’+C = M6 A’+B’+C’ = M7
Minterm of 3 variables

## Slide 18
3.3 Minterm and Maxterm Expansions
Sum of minterms
Minterm expansion
Standard sum of products
Canonical sum of products

## Slide 19: 3.3 Minterm and Maxterm Expansions
Maxterm of n variables
A sum of n literals in which each variable appears exactly once in either true or complemented form, but not both
Notation
Mi

## Slide 20: 3.3 Minterm and Maxterm Expansions
Row No. | A B C | Minterms | Maxterms
0 1 2 3 4 5 6 7 | 0 0 0 0 0 1 0 1 0 0 1 1 1 0 0 1 0 1 1 1 0 1 1 1 |  | A+B+C = M0 A+B+C’ = M1 A+B’+C = M2 A+B’+C’ = M3 A’+B+C = M4 A’+B+C’ = M5 A’+B’+C = M6 A’+B’+C’ = M7
Row No. | A B C | Minterms | Maxterms
0 1 2 3 4 5 6 7 | 0 0 0 0 0 1 0 1 0 0 1 1 1 0 0 1 0 1 1 1 0 1 1 1 |  | A+B+C = M0 A+B+C’ = M1 A+B’+C = M2 A+B’+C’ = M3 A’+B+C = M4 A’+B+C’ = M5 A’+B’+C = M6 A’+B’+C’ = M7
Maxterm of 3 variables

## Slide 21
3.3 Minterm and Maxterm Expansions
Product of maxterms
Maxterm expansion
Standard product of sums
Canonical product of sums

## Slide 22
3.3 Minterm and Maxterm Expansions
Finding Complement

## Slide 23
3.3 Minterm and Maxterm Expansions
Minterm and Maxterm expansions are complement each other

## Slide 24
3.3 Minterm and Maxterm Expansions
Introducing Missing Variables
Find the minterm expansion of
Maxterm expansion

## Slide 25: 3.4 Incompletely Specified Functions
If N1 output does not generate all possible combination of A, B, C, the output of N2(F) has don’t care values.
Truth Table with Don’t Cares
Don’t Care
A B C | f
0 0 0 | 1
0 0 1 | X
0 1 0 | 0
0 1 1 | 1
1 0 0 | 0
1 0 1 | 0
1 1 0 | X
1 1 1 | 1

## Slide 26: 3.4 Incompletely Specified Functions
When realize, assign values which will help simplify the function.
Case 1: assign ‘0’ on all X’s
Case 2: assign ‘1’ to the first X and ‘0’ to the second ‘X’
Case 3: assign ‘1’ on all X’s
The case 2 leads to the simplest function
Don’t Care
A B C | f
0 0 0 | 1
0 0 1 | X
0 1 0 | 0
0 1 1 | 1
1 0 0 | 0
1 0 1 | 0
1 1 0 | X
1 1 1 | 1

## Slide 27
3.4 Incompletely Specified Functions
Minterm expansion for incompletely specified function
Maxterm expansion for incompletely specified function
Notation for Don’t Care Terms
Don’t Cares
Don’t Cares
A B C | f
0 0 0 | 1
0 0 1 | X
0 1 0 | 0
0 1 1 | 1
1 0 0 | 0
1 0 1 | 0
1 1 0 | X
1 1 1 | 1

## Slide 28: 3.5 Design of Binary Adders and Subtractors
Truth Table for a Half Adder
Half Adder
Half
Adder
0 0 | 0 0
0 1 | 0 1
1 0 | 0 1
1 1 | 1 0
0 0 | 0 0
0 1 | 0 1
1 0 | 0 1
1 1 | 1 0

## Slide 29: 3.5 Design of Binary Adders and Subtractors
Truth Table for a Full Adder
Full Adder
Full
Adder
0 0 0 | 0 0
0 0 1 | 0 1
0 1 0 | 0 1
0 1 1 | 1 0
1 0 0 | 0 1
1 0 1 | 1 0
1 1 0 | 1 0
1 1 1 | 1 1
0 0 0 | 0 0
0 0 1 | 0 1
0 1 0 | 0 1
0 1 1 | 1 0
1 0 0 | 0 1
1 0 1 | 1 0
1 1 0 | 1 0
1 1 1 | 1 1

## Slide 30: 3.5 Design of Binary Adders and Subtractors
Implementation of Full Adder
Truth Table for a Full Adder
0 0 0 | 0 0
0 0 1 | 0 1
0 1 0 | 0 1
0 1 1 | 1 0
1 0 0 | 0 1
1 0 1 | 1 0
1 1 0 | 1 0
1 1 1 | 1 1
0 0 0 | 0 0
0 0 1 | 0 1
0 1 0 | 0 1
0 1 1 | 1 0
1 0 0 | 0 1
1 0 1 | 1 0
1 1 0 | 1 0
1 1 1 | 1 1

## Slide 31: 3.5 Design of Binary Adders and Subtractors
Implementation of Full Adder
X
Y
sum
Cin
X
Y
Cin
X
Y
Cin
Cout

## Slide 32: 3.5 Design of Binary Adders and Subtractors
Parallel Adder for 4 bit Binary Numbers
1 | 0 | 1 | 1 | 0 | 
 | 1 | 0 | 1 | 1 | 
 | 1 | 0 | 1 | 1 | 
1 | 0 | 1 | 1 | 0 | 
1 | 0 | 1 | 1 | 0 | 
 | 1 | 0 | 1 | 1 | 
 | 1 | 0 | 1 | 1 | 
1 | 0 | 1 | 1 | 0 | 
Full
Adder
Full
Adder
Full
Adder
Full
Adder

## Slide 33: 3.5 Design of Binary Adders and Subtractors
Parallel Adder for 4 bit Binary Numbers
1 | 0 | 1 | 1 | 0 | 
 | 1 | 0 | 1 | 1 | 
 | 1 | 0 | 1 | 1 | 
1 | 0 | 1 | 1 | 0 | 
1 | 0 | 1 | 1 | 0 | 
 | 1 | 0 | 1 | 1 | 
 | 1 | 0 | 1 | 1 | 
1 | 0 | 1 | 1 | 0 | 
4-bit Parallel Adder

## Slide 34: 3.5 Design of Binary Adders and Subtractors
Parallel Adder Composed of Four Full Adders
Carry Ripple Adder (slow!)
1 | 0 | 1 | 1 | 0 | 
 | 1 | 0 | 1 | 1 | 
 | 1 | 0 | 1 | 1 | 
1 | 0 | 1 | 1 | 0 | 
1 | 0 | 1 | 1 | 0 | 
 | 1 | 0 | 1 | 1 | 
 | 1 | 0 | 1 | 1 | 
1 | 0 | 1 | 1 | 0 | 
Full
Adder
Full
Adder
Full
Adder
Full
Adder
0

## Slide 35: 3.5 Design of Binary Adders and Subtractors
Full
Adder
Full
Adder
Full
Adder
Full
Adder
1
Ignore
Last
Carry
Binary Subtractor Using Full Adder
Subtraction is done by adding the 2’s complemented number to be subtracted.

## Slide 36
Summary
Conversion of Verbal Description to Boolean Equations
Combinational Logic Design Using a Truth Table
Minterm and Maxterm Expansions
Incompletely Specified Functions (Don’t care term)
Design of Binary Adders(Full adder) and Subtractors

## Slide 38
Part 2 Karnaugh Map
(K-Map)

## Slide 39: Objectives
Given a function (completely or in completely specified) of three to five variable, plot it on a Karnaugh map. The function may be given in minterm, maxterm, or algebraic form.
Determine the essential prime implicants of a function from a map.
Obtain the minimum sum-of-products or minimum product-of-sums form of a function from the map.
Determine all of the prime implicants of a function from a map.
Understand the relation between operations performed using the map and the corresponding algebraic operation.

## Slide 40: Karnaugh Maps
Difficult to apply in a systematic way.
Difficult to tell when you have arrived at a minimum solution.
Two Problems of Simplifying a Switching Function Using Algebraic Techniques
Karnaugh Map method and Quine-McCluskey Procdure
Easy and systematic to get a a minimum solution.

## Slide 41: 3.6 Minimum Forms of Switching Functions
Realizing a switching function using AND and OR gates
Sum-of-Products form

## Slide 42: 3.6 Minimum Forms of Switching Functions
What we want is a circuit with
Minimum number of gates
Minimum number of gate inputs
Minimum number of terms
Minimum number of literals
Minimum Sum-of-Products form
Sum-of-Products form

## Slide 43: 3.6 Minimum Forms of Switching Functions
Procedure for obtaining a minimum sum-of-products
Combine terms by using .
Do this repeatedly to eliminates as many literals as possible.
A given term may be used more than once because .

## Slide 44: 3.7 Two- and Three-Variable Karnaugh Maps
2-variable Karnaugh Map

## Slide 45: 3.7 Two- and Three-Variable Karnaugh Maps
A B | F
0 0 0 1 1 0 1 1 | 1 1 0 0
Example: Truth table and Karnaugh map for a two-variable function
(a)

## Slide 46: 3.7 Two- and Three-Variable Karnaugh Maps
A B C | F
0 0 0 0 0 1 0 1 0 0 1 1 1 0 0 1 0 1 1 1 0 1 1 1 | 0 0 1 1 1 0 1 0
(a)
Example: Truth table and Karnaugh map for a three-variable function

## Slide 47: 3.7 Two- and Three-Variable Karnaugh Maps
3-variable Karnaugh map
Minterms in adjacent squares differ in only one variable
Can be combined using the theorem .

## Slide 48: 3.7 Two- and Three-Variable Karnaugh Maps
Karnaugh Map of
Plot of minterm: mark 1
Plot of maxterm: mark 0
Plot of minterms and maxterms

## Slide 49: 3.7 Two- and Three-Variable Karnaugh Maps
Karnaugh maps for non-minterm product terms
term b
term bc’
term ac’

## Slide 50: 3.7 Two- and Three-Variable Karnaugh Maps
Karnaugh maps for non-minterm product terms

## Slide 51: 3.7 Two- and Three-Variable Karnaugh Maps
Simplification of a Three-Variable Function

## Slide 52: 3.7 Two- and Three-Variable Karnaugh Maps
Complement of a function
:
Replace 0 → 1
and 1 → 0

## Slide 53: 3.7 Two- and Three-Variable Karnaugh Maps
Function with two minimum forms

## Slide 54: 3.8 Four-Variable Karnaugh Maps
Location of minterms on four-variable Karnaugh map

## Slide 55: 3.8 Four-Variable Karnaugh Maps
Plot of a function

## Slide 56: 3.8 Four-Variable Karnaugh Maps
Simplification of four-variable function

## Slide 57: 3.8 Four-Variable Karnaugh Maps
Simplification of four-variable function

## Slide 58: 3.8 Four-Variable Karnaugh Maps
Simplification of an function with don’t care conditions
don’t care term

## Slide 59: 3.8 Four-Variable Karnaugh Maps
Find minimum product-of-sums by using Karnaugh map
Plot 1’s of f
Group 0’s in the map → f’
Apply DeMorgan’s law
Given

## Slide 60: 3.9 Determination of Minimum Expressions Using Essential Prime Implicants
Implicants of F
  Any product term in sum-of products form
Prime Implicants of F
  A product term which can not be combined with other terms to eliminate variable
Prime Implicants
Non-Prime Implicants

## Slide 61: 3.9 Determination of Minimum Expressions Using Essential Prime Implicants
Determination of Prime Implicants (PI)
A single 1 on a map can be a PI if it is not adjacent to any other 1’s.
Two adjacent 1’s if they are not contained in a group of four 1’s.
Four adjacent 1’s if they are not contained in a group of eight 1’s.
And so on…
Prime Implicants
Non-Prime Implicants

## Slide 62: 3.9 Determination of Minimum Expressions Using Essential Prime Implicants
Prime Implicants and Minimum Solution
ab

## Slide 63: 3.9 Determination of Minimum Expressions Using Essential Prime Implicants
Systematic Procedure for Selecting Prime Implicants
CD is chosen first
Other PI’s are chosen first

## Slide 64: 3.9 Determination of Minimum Expressions Using Essential Prime Implicants
Essential Prime Implicants (EPI)
  If a minterm is covered by only one PI, the PI is said to be an EPI
m5
m14
m2
BD, B’C, AC: EPI

## Slide 65
3.9 Determination of Minimum Expressions Using Essential Prime Implicants
Procedure for Selecting EPI
Loop all PI
Find minterm covered by only one PI
Select that PI as an EPI
Repeat step 2 and 3
1. m4 is covered by only BC’
2. m10 is covered by only AC
3. BC’ and AC are EPI
AB
CD
00
01
11
10
00
01
11
10
0
4
8
12
1
3
2
7
6
9
11
10
13
15
14
5
1
1
1
1
1
1
1
1
1
1
BC’
AC

## Slide 66: 3.9 Determination of Minimum Expressions Using Essential Prime Implicants
Systematic Approach for Finding EPIs
If a given minterm and all of the 1’s adjacent to it are covered by a single term, then that term is an EPI.
If all of the 1’s adjacent to a given minterm are not covered by a single term, then there are two or more PIs which cover that minterm, and we cannot say whether these PIs are essential or not without checking other minterms.

## Slide 67: 3.9 Determination of Minimum Expressions Using Essential Prime Implicants
Systematic Approach for Finding EPIs
AB
CD
00
01
11
10
00
01
11
10
0
4
8
12
1
3
2
7
6
9
11
10
13
15
14
5
1
1
1
1
1
1
1
1
Check adjacent 1’s for m0(10)
  No single term covers 10, 11, 12, 14.
  No EPIs
Check adjacent 1’s for 11
  A’C’ covers 11, 10, 15.
  A’C’ is an EPI.
A’C’
Check adjacent 1’s for 12
  A’B’D’ covers 12, 10.
  A’B’D’ is an EPI.
A’B’D’

## Slide 68: 3.9 Determination of Minimum Expressions Using Essential Prime Implicants
Systematic Approach for Finding EPIs
Check adjacent 1’s for 17
  No single term covers 17, 15, 115.
  No EPIs
AB
CD
00
01
11
10
00
01
11
10
0
4
8
12
1
3
2
7
6
9
11
10
13
15
14
5
1
1
1
1
1
1
1
1
A’C’
A’B’D’
Check adjacent 1’s for 111
  ACD covers 11, 10, 15.
  ACD is an EPI.
ACD
A’BD
A’BD or BCD is selected to include 17.
BCD

## Slide 69: 3.9 Determination of Minimum Expressions Using Essential Prime Implicants
Flowchart for Determining a Minimum SOP Using a Karnaugh Map
Choose a 1 which has not been covered.
Find all adjacent 1’s and X’s.
Are the chosen 1 and its adjacent 1’s and X’s covered by a single term?
That term is an EPI. Loop it.
All uncovered 1’s checked?
Find a minimum set of prime implicants which cover the remaining 1’s on the map.
Stop.
YES
NO
YES
NO

## Slide 70: 3.9 Determination of Minimum Expressions Using Essential Prime Implicants
AB’D’ covers 110 and its adjacent  EPI
AB’D’
110
16
X15
X7
19
113
15
18
14
X0
AB
CD
00
01
11
10
00
01
11
10
A’B covers 16 and its adjacent  EPI
A’B
AC’D is chosen for minimal cover  AC’D is not an EPI
AC’D

## Slide 71: 3.10 Five-Variable Karnaugh Maps
Two Layers of Four-Variable Karnaugh Map

## Slide 72: 3.10 Five-Variable Karnaugh Maps
Five Adjacent Terms
Four adjacent terms in the same layer
One adjacent term in the other layer

## Slide 73: Summary
Given a function (completely or in completely specified) of three to five variable, plot it on a Karnaugh map. The function may be given in minterm, maxterm, or algebraic form.
Determine the essential prime implicants of a function from a map.
Obtain the minimum sum-of-products or minimum product-of-sums form of a function from the map.
Determine all of the prime implicants of a function from a map.
Understand the relation between operations performed using the map and the corresponding algebraic operation.