## Slide 1
디지털시스템 및 마이크로 컴퓨터 I
4 주차 강의
Mar 22, 2021

## Slide 2
Part 1 Quine-McCluskey Method

## Slide 3
Find the prime implicants of a function by using the Quine-McCluskey method.
Given the prime implicants, find the essential prime implicants and a minimum sum-of-products expression for a function using a prime implicant chart.
Gate delays
Simulations
Objective

## Slide 4
Quine-McCluskey Method
Used when the number of variables is large
Provides systematic simplification procedure which can be readily programmed for a digital computer.
Quine-McCluskey Method
Eliminate as many literals as possible from each term by systematically applying the theorem
XY + XY’ = X
The resulting terms are called prime implicants
Use an implicant chart to select a minimum set of prime implicants
Reduction Procedure

## Slide 5: 4.1 Determination of Prime Implicants
Convert the given function into a sum-of minterms form
The minterms are represented in binary notation
The two terms can be combined using if two terms differ in exactly one variable.

## Slide 6: 4.1 Determination of Prime Implicants
Example 1
Two terms differ in two variables, so it cannot be combined.
The dash() indicates a missing variable
Example 2

## Slide 7
4.1 Determination of Prime Implicants
Given binary minterms are sorted into groups according to the number of 1’s in each term.
Example
group 0 | 0 | 0000
group 1 | 1 | 0001
 | 2 | 0010
 | 8 | 1000
group 2 | 5 | 0101
 | 6 | 0110
 | 9 | 1001
 | 10 | 1010
group 3 | 7 | 0111
 | 14 | 1110
 | 0000
 | 0001
 | 0010
 | 0101
 | 0110
 | 0111
 | 1000
 | 1001
 | 1010
 | 1110
 | 0000
 | 0001
 | 0010
 | 0101
 | 0110
 | 0111
 | 1000
 | 1001
 | 1010
 | 1110

## Slide 8: 4.1 Determination of Prime Implicants
group 0 | 0 | 0000 | 
group 1 | 1 2 8 | 0001 0010 1000 | 
group 2 | 5 6 9 10 | 0101 0110 1001 1010 | 
group 3 | 7 14 | 0111 1110 | 
0, 1 | 000- | 
0, 2 | 00-0 | 
0, 8 | -000 | 
1, 5 | 0-01 | 
1, 9 | -001 | 
2, 6 | 0-10 | 
2,10 | -010 | 
8, 9 | 100- | 
8,10 | 10-0 | 
5, 7 | 01-1 | 
6, 7 | 011- | 
6,14 | -110 | 
10,14 | 1-10 | 
Determination of Prime Implicants (1)
0, 1, 8, 9 0, 2, 8,10 0, 8, 1, 9 0, 8, 2,10 | -00- -0-0 -00- -0-0
2, 6,10,14 2,10, 6,14 | --10 --10
Column I
Column II
Column III

## Slide 9: 4.1 Determination of Prime Implicants
group 0 | 0 | 0000 | √
group 1 | 1 2 8 | 0001 0010 1000 | √
 |  |  | √
 |  |  | √
group 2 | 5 6 9 10 | 0101 0110 1001 1010 | √
 |  |  | √
 |  |  | √
 |  |  | √
group 3 | 7 14 | 0111 1110 | √
 |  |  | √
0, 1 | 000- | 
0, 2 | 00-0 | 
0, 8 | -000 | 
1, 5 | 0-01 | 
1, 9 | -001 | 
2, 6 | 0-10 | 
2,10 | -010 | 
8, 9 | 100- | 
8,10 | 10-0 | 
5, 7 | 01-1 | 
6, 7 | 011- | 
6,14 | -110 | 
10,14 | 1-10 | 
Determination of Prime Implicants (2)
0, 1, 8, 9 0, 2, 8,10 0, 8, 1, 9 0, 8, 2,10 | -00- -0-0 -00- -0-0
2, 6,10,14 2,10, 6,14 | --10 --10
Column I
Column II
Column III

## Slide 10: 4.1 Determination of Prime Implicants
group 0 | 0 | 0000 | √
group 1 | 1 2 8 | 0001 0010 1000 | √
 |  |  | √
 |  |  | √
group 2 | 5 6 9 10 | 0101 0110 1001 1010 | √
 |  |  | √
 |  |  | √
 |  |  | √
group 3 | 7 14 | 0111 1110 | √
 |  |  | √
0, 1 | 000- | √
0, 2 | 00-0 | √
0, 8 | -000 | √
1, 5 | 0-01 | 
1, 9 | -001 | √
2, 6 | 0-10 | √
2,10 | -010 | √
8, 9 | 100- | √
8,10 | 10-0 | √
5, 7 | 01-1 | 
6, 7 | 011- | 
6,14 | -110 | √
10,14 | 1-10 | √
Determination of Prime Implicants (3)
0, 1, 8, 9 0, 2, 8,10 0, 8, 1, 9 0, 8, 2,10 | -00- -0-0 -00- -0-0
2, 6,10,14 2,10, 6,14 | --10 --10
Column I
Column II
Column III

## Slide 11: 4.1 Determination of Prime Implicants
group 0 | 0 | 0000 | √
group 1 | 1 2 8 | 0001 0010 1000 | √
 |  |  | √
 |  |  | √
group 2 | 5 6 9 10 | 0101 0110 1001 1010 | √
 |  |  | √
 |  |  | √
 |  |  | √
group 3 | 7 14 | 0111 1110 | √
 |  |  | √
0, 1 | 000- | √
0, 2 | 00-0 | √
0, 8 | -000 | √
1, 5 | 0-01 | 
1, 9 | -001 | √
2, 6 | 0-10 | √
2,10 | -010 | √
8, 9 | 100- | √
8,10 | 10-0 | √
5, 7 | 01-1 | 
6, 7 | 011- | 
6,14 | -110 | √
10,14 | 1-10 | √
Determination of Prime Implicants (4)
0, 1, 8, 9 0, 2, 8,10 0, 8, 1, 9 0, 8, 2,10 | -00- -0-0 -00- -0-0
2, 6,10,14 2,10, 6,14 | --10 --10
Column I
Column II
Column III

## Slide 12: 4.2 The Prime Implicant Chart
 |  | 0 | 1 | 2 | 5 | 6 | 7 | 8 | 9 | 10 | 14
(0,1,8,9) |  | x | x |  |  |  |  | x | x |  | 
(0,2,8,10) |  | x |  | x |  |  |  | x |  | x | 
(2,6,10,14) |  |  |  | x |  | x |  |  |  | x | x
(1,5) |  |  | x |  | x |  |  |  |  |  | 
(5,7) |  |  |  |  | x |  | x |  |  |  | 
(6,7) |  |  |  |  |  | x | x |  |  |  | 
 |  | 0 | 1 | 2 | 5 | 6 | 7 | 8 | 9 | 10 | 14
(0,1,8,9) |  | x | x |  |  |  |  | x | x |  | 
(0,2,8,10) |  | x |  | x |  |  |  | x |  | x | 
(2,6,10,14) |  |  |  | x |  | x |  |  |  | x | x
(1,5) |  |  | x |  | x |  |  |  |  |  | 
(5,7) |  |  |  |  | x |  | x |  |  |  | 
(6,7) |  |  |  |  |  | x | x |  |  |  | 
Prime Implicant Chart (Table 6-2)
Select Essential Prime Implicants

## Slide 13: 4.2 The Prime Implicant Chart
 |  | 0 | 1 | 2 | 5 | 6 | 7 | 8 | 9 | 10 | 14
(0,1,8,9) |  | x | x |  |  |  |  | x |  |  | 
(0,2,8,10) |  | x |  | x |  |  |  | x |  | x | 
(2,6,10,14) |  |  |  | x |  | x |  |  |  | x | 
(1,5) |  |  | x |  | x |  |  |  |  |  | 
(5,7) |  |  |  |  | x |  | x |  |  |  | 
(6,7) |  |  |  |  |  | x | x |  |  |  | 
 |  | 0 | 1 | 2 | 5 | 6 | 7 | 8 | 9 | 10 | 14
(0,1,8,9) |  | x | x |  |  |  |  | x |  |  | 
(0,2,8,10) |  | x |  | x |  |  |  | x |  | x | 
(2,6,10,14) |  |  |  | x |  | x |  |  |  | x | 
(1,5) |  |  | x |  | x |  |  |  |  |  | 
(5,7) |  |  |  |  | x |  | x |  |  |  | 
(6,7) |  |  |  |  |  | x | x |  |  |  | 
Prime Implicant Chart (Table 6-2)
Select Essential Prime Implicants

## Slide 14: 4.2 The Prime Implicant Chart
 |  |  | 0 | 1 | 2 | 5 | 6 | 7 | 8 | 9 | 10 | 14
(0,1,8,9) | √ |  | x | x |  |  |  |  | x |  |  | 
(0,2,8,10) |  |  | x |  | x |  |  |  | x |  | x | 
(2,6,10,14) | √ |  |  |  | x |  | x |  |  |  | x | 
(1,5) |  |  |  | x |  | x |  |  |  |  |  | 
(5,7) |  |  |  |  |  | x |  | x |  |  |  | 
(6,7) |  |  |  |  |  |  | x | x |  |  |  | 
 |  |  | 0 | 1 | 2 | 5 | 6 | 7 | 8 | 9 | 10 | 14
(0,1,8,9) | √ |  | x | x |  |  |  |  | x |  |  | 
(0,2,8,10) |  |  | x |  | x |  |  |  | x |  | x | 
(2,6,10,14) | √ |  |  |  | x |  | x |  |  |  | x | 
(1,5) |  |  |  | x |  | x |  |  |  |  |  | 
(5,7) |  |  |  |  |  | x |  | x |  |  |  | 
(6,7) |  |  |  |  |  |  | x | x |  |  |  | 
Prime Implicant Chart (Table 6-2)
Select Essential Prime Implicants

## Slide 15: 4.2 The Prime Implicant Chart
 |  |  | 0 | 1 | 2 | 5 | 6 | 7 | 8 | 9 | 10 | 14
(0,1,8,9) | √ |  | x | x |  |  |  |  | x |  |  | 
(0,2,8,10) |  |  | x |  | x |  |  |  | x |  | x | 
(2,6,10,14) | √ |  |  |  | x |  | x |  |  |  | x | 
(1,5) |  |  |  | x |  | x |  |  |  |  |  | 
(5,7) | √ |  |  |  |  | x |  | x |  |  |  | 
(6,7) |  |  |  |  |  |  | x | x |  |  |  | 
 |  |  | 0 | 1 | 2 | 5 | 6 | 7 | 8 | 9 | 10 | 14
(0,1,8,9) | √ |  | x | x |  |  |  |  | x |  |  | 
(0,2,8,10) |  |  | x |  | x |  |  |  | x |  | x | 
(2,6,10,14) | √ |  |  |  | x |  | x |  |  |  | x | 
(1,5) |  |  |  | x |  | x |  |  |  |  |  | 
(5,7) | √ |  |  |  |  | x |  | x |  |  |  | 
(6,7) |  |  |  |  |  |  | x | x |  |  |  | 
Prime Implicant Chart (Table 6-2)
The resulting minimum sum of products is
Select Essential Prime Implicants

## Slide 16: 4.3 Gate Delays
Propagation Delay in an Inverter
Few ns

## Slide 17: 4.3 Gate Delays
Timing Diagram for AND-NOR Circuit
Assume: each gate has 20 ns propagation delay time

## Slide 18: 4.3 Gate Delays - Hazards
Detection of a 1-Hazard
Assume: Each gate has 10 ns pro. delay time
A = C = 1
Hazard occurs when B changes
while A = C = 1

## Slide 19
Circuit with Hazard Removed
4.3 Gate Delays - Hazards

## Slide 20
AND and OR Functions for Four-Valued Simulation
4.4 Simulation
X: Unknown, Z: High Impedance
∙ | 0 | 1 | X | Z
0 | 0 | 0 | 0 | 0
1 | 0 | 1 | X | X
X | 0 | X | X | X
Z | 0 | X | X | X
+ | 0 | 1 | X | Z
0 | 0 | 1 | X | X
1 | 1 | 1 | 1 | 1
X | X | 1 | X | X
Z | X | 1 | X | X

## Slide 21: Summary
Find the prime implicants of a function by using the Quine-McCluskey method.
Given the prime implicants, find the essential prime implicants and a minimum sum-of-products expression for a function using a prime implicant chart.
Gate delays
Simulations

## Slide 23
Part 2
Multiplexers, Three-State Buffers, Decoders, Encoders,
Programmable Logic Devices

## Slide 24: Objectives
IC (Integrated Circuit)
  SSI (Small-Scale Integration)
  MSI (Medium-Scale Integration)
  LSI (Large-Scale Integration)
  VLSI (Very-Large-Scale Integration)
Multiplexers
Three-state Buffer
Decoders and Encoders
ROMs
PLD
PLA
CPLD
FPGA

## Slide 25: 4.5 Multiplexers
2-to-1 Multiplexer and Switch Analog
Logic equation for the 2-to-1 MUX
Multiplexer (MUX, Data Selector)

## Slide 26: 4.5 Multiplexers
4-to-1 Multiplexer
Logic equation for the 4-to-1 MUX

## Slide 27: 4.5 Multiplexers
8-to-1 Multiplexer
Logic equation for the 8-to-1 MUX

## Slide 28: 4.5 Multiplexers
2n-to-1 Multiplexer
Logic equation for the 2n - to - 1 MUX
: minterm of the n control variables
: corresponding data input

## Slide 29: 4.5 Multiplexers
Quadruple 2-to-1 Multiplexer Used to Select Data

## Slide 30: 4.5 Multiplexers
Quad Multiplexer with Bus Inputs and Output
X, Y : Bus input
Z : Bus output

## Slide 31: 4.6 Three-State Buffers
Gate Circuit with Added Buffer
The logic of the buffer input and output are the same (F = C)
Buffer is used to increase driving capability

## Slide 32: 4.6 Three-State Buffers

## Slide 33: 4.6 Three-State Buffers
Three-State Buffer
The output is enabled when B = 1, disabled when B = 0
Tri-State Buffer
High-impedance (Hi-Z) state

## Slide 34: 4.6 Three-State Buffers
Four Kinds of Three-State Buffers
B A | C
0 0 0 1 1 0 1 1 | Z Z 0 1
(a)
B A | C
0 0 0 1 1 0 1 1 | Z Z 1 0
(b)
B A | C
0 0 0 1 1 0 1 1 | 0 1 Z Z
(c)
B A | C
0 0 0 1 1 0 1 1 | 1 0 Z Z
(d)

## Slide 35: 4.6 Three-State Buffers
Data Selection Using Three-State Buffers

## Slide 36: 4.6 Three-State Buffers
Circuit with Two Three-State Buffers
S1 | X | S2 0 | 1 | Z
X 0 1 Z | X X X X | X 0 X 0 | X X 1 1 | X 0 1 Z
X = Unknown
S1
S2

## Slide 37: 4.6 Three-State Buffers
4-Bit Adder with Four Sources for One Operand
Four Sources

## Slide 38: 4.6 Three-State Buffers
Integrated Circuit with Bi-Directional Input/Output Pin

## Slide 39: 4.7 Decoders and Encoders
3-to-8 Line Decoder
a b c | y0 | y1 | y2 | y3 | y4 | y5 | y6 | y7
0 0 0 0 0 1 0 1 0 0 1 1 1 0 0 1 0 1 1 1 0 1 1 1 | 1 0 0 0 0 0 0 0 | 0 1 0 0 0 0 0 0 | 0 0 1 0 0 0 0 0 | 0 0 0 1 0 0 0 0 | 0 0 0 0 10 0 0 | 0 0 0 0 0 10 0 | 0 0 0 0 0 0 10 | 0 0 0 0 0 0 0 1

## Slide 40: 4.7 Decoders and Encoders
4-to-10 Line Decoder (74LS42)

## Slide 41: 4.7 Decoders and Encoders
4-to-10 Line Decoder (74LS42)

## Slide 42: 4.7 Decoders and Encoders
8-to-3 Priority Encoder
y0 | y1 | y2 | y3 | y4 | y5 | y6 | y7 | a | b | c | d
0 1 X X X X X X X | 0 0 1 X X X X X X | 0 0 0 1 X X X X X | 0 0 0 0 1 X X X X | 0 0 0 0 01 X X X | 0 0 0 0 0 0 1 X X | 0 0 0 0 0 0 0 1 X | 0 0 0 0 0 0 0 0 1 | 0 0 0 0 0 1 1 1 1 | 0 0 0 1 1 0 0 1 1 | 0 0 1 0 1 0 1 0 1 | 0 1 1 1 1 1 1 1 1

## Slide 43: 4.8 Read-Only Memories
An 8-Word x 4-Bit ROM
A | B | C |  |  | F0 | F1 | F2 | F3
0 0 0 0 1 1 1 1 | 0 0 1 1 0 0 1 1 | 0 1 0 1 0 1 0 1 |  |  | 1 1 0 0 1 0 1 0 | 0 0 1 1 1 0 1 1 | 1 1 1 0 0 0 1 0 | 0 0 1 1 0 1 1 1
(a) Block diagram
(b) Truth table for ROM
typical data stored in ROM
(23 words of
4bits each)

## Slide 44: 4.8 Read-Only Memories
Read-Only Memory with n Inputs and m Outputs
n input Variables |  |  |  | m output Variables |  |  | 
00 00 00 00 11 11 11 11 | · · · · · · · · · · · · · · · · · · · · · | 00 01 10 11 00 01 10 11 |  |  | 100 010 101 110 001 110 011 111 | · · · · · · · · · · · · · · · · · · · · · | 110 111 101 010 · · 011 110 000 101
typical data array stored in ROM
(2n words of m bits each)

## Slide 45: 4.8 Read-Only Memories
An 8-Word x 4-Bit ROM
A | B | C |  |  | F0 | F1 | F2 | F3
0 0 0 0 1 1 1 1 | 0 0 1 1 0 0 1 1 | 0 1 0 1 0 1 0 1 |  |  | 1 1 0 0 1 0 1 0 | 0 0 1 1 1 0 1 1 | 1 1 1 0 0 0 1 0 | 0 0 1 1 0 1 1 1
(b) Truth table for ROM
Equivalent OR Gate for F0

## Slide 46: 4.8 Read-Only Memories
Types of ROMs
Mask ROM
Programmable ROM
Electrically Erasable Programmable ROM
Flash Memory

## Slide 47: 4.9 Programmable Logic Devices (PLD)
Programmable Logic Array (PLA) Structure
Both AND array and OR array are programmable.

## Slide 48: 4.9 Programmable Logic Devices (PLD)
Programmable Array Logic (PAL)
AND array is programmable and OR array is fixed.
PAL

## Slide 49: 4.9 Programmable Logic Devices (PLD)
Programmable Array Logic (PAL)
logically equal
AND array is programmable and OR array is fixed.

## Slide 50: 4.9 Programmable Logic Devices (PLD)
Connections to the AND gate inputs in a PAL is represented by X
Programmable Array Logic

## Slide 51: 4.9 Programmable Logic Devices (PLD)
PAL Segment
Unprogrammed
Programmed

## Slide 52: 4.9 Programmable Logic Devices (PLD)
Implementation of a Full Adder Using a PAL

## Slide 53: 4.10 Complex Programmable Logic Devices (CPLD)
Basic Architecture of Xilinx XCR3064XL CPLD
4 Function Blocks: programmable AND-OR array
16 Macrocells per Block: flip-flop and MUXs

## Slide 54: 4.10 Complex Programmable Logic Devices (CPLD)
CPLD Function Block and Macrocell (A Simplified Version of XCR3064XL)

## Slide 55: 4.11 Field Programmable Gate Arrays (FPGA)
Layout of a typical FPGA

## Slide 56: 4.11 Field Programmable Gate Arrays (FPGA)
Simplified Configurable Logic Block (CLB)
LUT: Look Up Table
Reprogrammable
Function Generator
Function Generator
Combinational
Output
Combinational
Output
Flip-flop Output
Flip-flop Output

## Slide 57
Implementation of a Function Generator (Lookup Table, LUT)
4.11 Field Programmable Gate Arrays (FPGA)

## Slide 58: Summary
IC (Integrated Circuit)
  SSI (Small-Scale Integration)
  MSI (Medium-Scale Integration)
  LSI (Large-Scale Integration)
  VLSI (Very-Large-Scale Integration)
Multiplexers
Three-state Buffer
Decoders and Encoders
ROMs
PLD
PLA
CPLD
FPGA