## Slide 1
디지털시스템 및 마이크로 컴퓨터 I
7 주차 강의
Apr., 07, 2021
인제대학교 의용공학부
조 종만 교수

## Slide 2
Unit 12 Registers and Counters

## Slide 3
Part 1 Registers

## Slide 4
Objectives
Explain the operation of registers.
Understand how to transfer data between registers using tri-state bus.
Explain the shift register operation, how to build them and analyze operation.
Construct a timing diagram for a shift register.
Explain the operation of binary counters.
How to build them using F/F and gates and analyze operation.
Given the present state and desired next state of F/F, determine the required F/F/ inputs
Given the desired counting sequence for a counter, derive F/F input equations.
Explain the procedures used for deriving F/F input equation.
Construct a timing diagram for a counter by tracing signals through the circuit.

## Slide 5
Registers and Counters
Register
  A group of flip-flops
  Use a common clock input
  Used to store and shift binary data
Counter
  A group of flip-flops
  Change states in a prescribed sequence

## Slide 6
Registers and Register Transfers
Load signal ANDed with Clk signal → may cause timing problems
ClrN signal for asynchronous clear
4-Bit D Flip-Flop Registers with Data, Load, Clear, and Clock inputs

## Slide 7
Registers and Register Transfers
4-Bit D Flip-Flop Registers with Data, Load, Clear, and Clock inputs
Load signal is applied to CE (Clock Enable) pin

## Slide 8
Registers and Register Transfers
4-Bit D Flip-Flop Registers with Data, Load, Clear, and Clock inputs
Symbol
Bus
Bus
4
4
ClrN
CE
Clr
Q
Load
Clk
D

## Slide 9
Data Transfer Between Registers
Registers and Register Transfers

## Slide 10
Data Transfer Between Registers (A → Q)
EN = 1
Load = 1
Registers and Register Transfers

## Slide 11
Data Transfer Between Registers (B → Q)
EN = 0
Load = 1
Registers and Register Transfers

## Slide 12
8-Bit Register with Tri-State Output
Registers and Register Transfers

## Slide 13
Data Transfer Using a Tri-State Bus
Registers and Register Transfers

## Slide 14: Shift Registers
4-bit Right-Shift Register
Shifting occurs when Shift = 1
t0
t1
t2
t3
t4
( ) 0 1 0 1 →
( ) 1 0 1 0 →
( ) 1 1 0 1 →
( ) 0 1 1 0 →
( ) 1 0 1 1
t0
t1
t2
t3
t4
Q3 Q2 Q1 Q0

## Slide 15: Shift Registers
8-Bit Serial-in, Serial-out Shift Register

## Slide 16: Shift Registers
Typical Timing Diagram for Shift Register

## Slide 17: Shift Registers
Parallel-in, Parallel-Out Right Shift Register

## Slide 18: Shift Registers
Parallel-in, Parallel-Out Right Shift Register
Inputs Sh (Shift) L(Load) | Next State Q3+ Q2+ Q1+ Q0+ | Action
0 0 0 1 1 X | Q3 Q2 Q1 Q0 D3 D2 D1 D0 SI Q3 Q2 Q1 | No change Load Right shift

## Slide 19: Shift Registers
The Next-state Equations for the Shifter Register
Typical Application of the Shifter Register
Conversion of parallel data to serial data

## Slide 20: Shift Registers
Timing Diagram for Shift Register
load
shift
shift
shift
no change

## Slide 21: Shift Registers
Shift Register with Inverted Feedback  Johnson Counter, Twisted Ring Counter
A 3-bit shift register
Successive states
Initial states = 000
Initial states = 010

## Slide 22
Part 2 Counters

## Slide 23: Design of Binary Counters
Counter
Synchronous counter
  State changes occur simultaneously
Asynchronous counter (Ripple counter)
  One flip-flop triggers the next flip-flop in line

## Slide 24: Design of Binary Counters
Asynchronous Counter (Ripple Counter)
Synchronous Counter

## Slide 25: Design of Binary Counters
A binary counter using three T F/F to count clock pulses
Design of a 3-bit Synchronous Binary Counter by Inspection of Counting Sequence
C B A
0 0 0
0 0 1
0 1 0
0 1 1
1 0 0
1 0 1
1 1 0
1 1 1
0 0 0
…
Counting
Sequence
To determine the flip-flop inputs – TA, TB, TC
A changes state for every clock input
B changes state if A = 1
C changes state if A = 1 and B = 1
→ TC = A AND B
→ TA = 1
→ TB = A

## Slide 26: Design of Binary Counters
A binary counter using three T F/F to count clock pulses
TC = A AND B
TA = 1
TB = A
Design of a 3-bit Synchronous Binary Counter by Inspection of Counting Sequence

## Slide 27: Design of Binary Counters
State Table for 3-bit Binary Counter
Design of a 3-bit Synchronous Binary Counter by Using a State Table
Present State C B A | Next State Flip-Flop Inputs C+ B+ A+ TC TB TA
0 0 0 0 0 1 0 1 0 0 1 1 1 0 0 1 0 1 1 1 0 1 1 1 | 0 0 1 0 0 1 0 1 0 0 1 1 0 1 1 0 0 1 1 0 0 1 1 1 1 0 1 0 0 1 1 1 0 0 1 1 1 1 1 0 0 1 0 0 0 1 1 1
A binary counter using three T F/F to count clock pulses

## Slide 28: Design of Binary Counters
Karnaugh Map for 3-bit Synchronous Binary Counter
TA = 1, TB = A, TC = AB
Design of a 3-bit Synchronous Binary Counter by Using a State Table
A binary counter using three T F/F to count clock pulses

## Slide 29: Design of Binary Counters
3-bit Synchronous Binary Counter with D Flip-Flops
To convert each D flip-flop to a T flip-flop by adding XOR gates

## Slide 30: Design of Binary Counters
3-bit Synchronous Binary Counter with D Flip-Flops
3-bit Synchronous Binary Counter with D Flip-Flops
To derive the D flip-flop input from the state table
Present State C B A | Next State Flip-Flop Inputs C+ B+ A+ DC DB DA
0 0 0 0 0 1 0 1 0 0 1 1 1 0 0 1 0 1 1 1 0 1 1 1 | 0 0 1 0 0 1 0 1 0 0 1 0 0 1 1 0 1 1 1 0 0 1 0 0 1 0 1 1 0 1 1 1 0 1 1 0 1 1 1 1 1 1 0 0 0 0 0 0
Q+ = D

## Slide 31: Design of Binary Counters
The D input equations derived from the maps are
Karnaugh Maps for D Flip-Flops
3-bit Synchronous Binary Counter with D Flip-Flops

## Slide 32: Design of Binary Counters
3-bit Synchronous Binary Counter with D Flip-Flops

## Slide 33: Design of Binary Counters
When U = 1, Up counting
When D = 1, Down counting
3-bit Synchronous Binary Up-Down Counter
State Table
CBA | C+B+A+ | 
 | U | D
000 | 001 | 111
001 | 010 | 000
010 | 011 | 001
011 | 100 | 010
100 | 101 | 011
101 | 110 | 100
110 | 111 | 101
111 | 000 | 110
State Graph

## Slide 34: Design of Binary Counters
3-bit Synchronous Binary Up-Down Counter Using D flip-flops
Logic Equations
State Table
CBA | C+B+A+ | 
 | U | D
000 | 001 | 111
001 | 010 | 000
010 | 011 | 001
011 | 100 | 010
100 | 101 | 011
101 | 110 | 100
110 | 111 | 101
111 | 000 | 110

## Slide 35: Design of Binary Counters
3-bit Synchronous Binary Up-Down Counter Using D flip-flops
Logic Equations

## Slide 36: Counters for Other Sequences
Form a state table.
  Next states for each present states
2. Plot the next-state maps from the table.
3. Plot a T input map for each F/F .
4. Find the T input equations from the maps
5. Realize the circuit.
Design of Non-Straight Binary Counter Using T Flip-Flops
State Graph for Counter

## Slide 37: Counters for Other Sequences
Design of Non-Straight Binary Counter Using T Flip-Flops
State Graph for Counter
State Table
Present State C B A | Next State C+ B+ A+
0 0 0 0 0 1 0 1 0 0 1 1 1 0 0 1 0 1 1 1 0 1 1 1 | 1 0 0 - - - 0 1 1 0 0 0 1 1 1 - - - - - - 0 1 0

## Slide 38: Counters for Other Sequences
Design of Non-Straight Binary Counter Using T Flip-Flops
Flip-Flop Inputs
Present State C B A | Next State Flip-Flop Inputs C+ B+ A+ TC TB TA
0 0 0 0 0 1 0 1 0 0 1 1 1 0 0 1 0 1 1 1 0 1 1 1 | 1 0 0 1 0 0 - - - - - - 0 1 1 0 0 1 0 0 0 0 1 1 1 1 1 0 1 1 - - - - - - - - - - - - 0 1 0 1 0 1
T Q | Q+
0 0 0 1 1 0 1 1 | 0 1 1 0

## Slide 39: Counters for Other Sequences
Design of Non-Straight Binary Counter Using T Flip-Flops
Flip-Flop Input Functions
C BA | 0 | 1
00 | 1 | 0
01 | x | x
11 | 0 | 1
10 | 0 | x
 | TC | 
C BA | 0 | 1
00 | 0 | 1
01 | x | x
11 | 1 | 0
10 | 0 | x
 | TB | 
C BA | 0 | 1
00 | 0 | 1
01 | x | x
11 | 1 | 1
10 | 1 | x
 | TA | 
Flip-Flop Inputs
Present State C B A | Next State Flip-Flop Inputs C+ B+ A+ TC TB TA
0 0 0 0 0 1 0 1 0 0 1 1 1 0 0 1 0 1 1 1 0 1 1 1 | 1 0 0 1 0 0 - - - - - - 0 1 1 0 0 1 0 0 0 0 1 1 1 1 1 0 1 1 - - - - - - - - - - - - 0 1 0 1 0 1

## Slide 40: Counters for Other Sequences
Design of Non-Straight Binary Counter Using T Flip-Flops

## Slide 41: Counters for Other Sequences
Timing Diagram for Non-Straight Binary Counter Using T Flip-Flops
Clock

## Slide 42: Counters for Other Sequences
CBA = 001, 101, 110
Analysis for Unused States
Timing Diagram for Non-Straight Binary Counter Using T Flip-Flops
C BA | 0 | 1
00 | 1 | 0
01 | x | x
11 | 0 | 1
10 | 0 | x
 | TC | 
C BA | 0 | 1
00 | 0 | 1
01 | x | x
11 | 1 | 0
10 | 0 | x
 | TB | 
C BA | 0 | 1
00 | 0 | 1
01 | x | x
11 | 1 | 1
10 | 1 | x
 | TA | 

## Slide 43: Counters for Other Sequences
Analysis for Unused States
CBA = 001, 101, 110
110
101
Timing Diagram for Non-Straight Binary Counter Using T Flip-Flops

## Slide 44: Counters for Other Sequences
Design of Non-Straight Binary Counter Using D Flip-Flops
State Graph for Counter
State Table
Present State C B A | Next State C+ B+ A+
0 0 0 0 0 1 0 1 0 0 1 1 1 0 0 1 0 1 1 1 0 1 1 1 | 1 0 0 - - - 0 1 1 0 0 0 1 1 1 - - - - - - 0 1 0

## Slide 45: Counters for Other Sequences
Design of Non-Straight Binary Counter Using D Flip-Flops
Flip-Flop Input Function for D Flip-Flop: Q+ = D
C BA | 0 | 1
00 | 1 | 1
01 | x | x
11 | 0 | 0
10 | 0 | x
 | C+ | 
C BA | 0 | 1
00 | 0 | 1
01 | x | x
11 | 0 | 1
10 | 1 | x
 | B+ | 
C BA | 0 | 1
00 | 0 | 1
01 | x | x
11 | 0 | 0
10 | 1 | x
 | A+ | 
State Table
Present State C B A | Next State C+ B+ A+
0 0 0 0 0 1 0 1 0 0 1 1 1 0 0 1 0 1 1 1 0 1 1 1 | 1 0 0 - - - 0 1 1 0 0 0 1 1 1 - - - - - - 0 1 0

## Slide 46: Counters for Other Sequences
Design of Non-Straight Binary Counter Using D Flip-Flops

## Slide 47: Counter Design Using S-R Flip-Flops
S-R Flip-Flop Inputs
(a)
(b)
(c)
S R Q | Q+
0 0 0 | 0
0 0 1 | 1
0 1 0 | 0
0 1 1 | 0
1 0 0 | 1
1 0 1 | 1
1 1 0 | -
1 1 1 | -
Q Q+ | S R
0 0 | 0 0
 | 0 1
0 1 | 0
1 0 | 0 1
1 1 | 0 0
 | 1 0
Q Q+ | S R
0 0 | 0 X
0 1 | 0
0 | 0 1
1 1 | X 0
not allowed

## Slide 48: Counter Design Using S-R Flip-Flops
Design of Non-Straight Binary Counter Using S-R Flip-Flops
Q Q+ | S R
0 0 | 0 X
0 1 | 0
0 | 0 1
1 1 | X 0
C B A | C+ B+ A+ | SC RC | SB RB | SA RA
0 0 0 | 1 0 0 | 0 | 0 X | 0 X
0 0 1 | - - - | X X | X X | X X
0 1 0 | 0 1 1 | 0 X | X 0 | 0
0 1 1 | 0 0 0 | 0 X | 0 1 | 0 1
1 0 0 | 1 1 1 | X 0 | 0 | 0
1 0 1 | - - - | X X | X X | X X
1 1 0 | - - - | X X | X X | X X
1 1 1 | 0 1 0 | 0 1 | X 0 | 0 1

## Slide 49: Counter Design Using S-R Flip-Flops
Design of Non-Straight Binary Counter Using S-R Flip-Flops

## Slide 50: Counter Design Using S-R Flip-Flops
Design of Non-Straight Binary Counter Using S-R Flip-Flops

## Slide 51: Counter Design Using J-K Flip-Flops
J-K Flip-Flop Inputs
(a)
(b)
(c)
J K Q | Q+
0 0 0 | 0
0 0 1 | 1
0 1 0 | 0
0 1 1 | 0
1 0 0 | 1
1 0 1 | 1
1 1 0 | 1
1 1 1 | 0
Q Q+ | J K
0 0 | 0 0
 | 0 1
0 1 | 0
 | 1
1 0 | 0 1
 | 1 1
1 1 | 0 0
 | 1 0
Q Q+ | J K
0 0 | 0 X
0 1 | X
0 | X 1
1 1 | X 0

## Slide 52: Counter Design Using J-K Flip-Flops
Design of Non-Straight Binary Counter Using J-K Flip-Flops
Q Q+ | J K
0 0 | 0 X
0 1 | X
0 | X 1
1 1 | X 0
C B A | C+ B+ A+ | JC KC | JB KB | JA KA
0 0 0 | 1 0 0 | X | 0 X | 0 X
0 0 1 | - - - | X X | X X | X X
0 1 0 | 0 1 1 | 0 X | X 0 | X
0 1 1 | 0 0 0 | 0 X | X 1 | X 1
1 0 0 | 1 1 1 | X 0 | X | X
1 0 1 | - - - | X X | X X | X X
1 1 0 | - - - | X X | X X | X X
1 1 1 | 0 1 0 | X 1 | X 0 | X 1

## Slide 53: Counter Design Using J-K Flip-Flops
Design of Non-Straight Binary Counter Using J-K Flip-Flops

## Slide 54: Counter Design Using J-K Flip-Flops
Design of Non-Straight Binary Counter Using J-K Flip-Flops