## Slide 1
디지털시스템 및 마이크로 컴퓨터 I
8 주차 강의
Apr., 15, 2021
인제대학교 의용공학부
조 종만 교수

## Slide 2
Part 1 Analysis of Clocked Sequential Circuits

## Slide 3: Objectives
For a given a sequential circuit
  Write the next-state equations for the flip-flops
  Derive the state graph or state table.
  Using the state graph, determine
    The state sequence
    Output sequence
Mealy machine and Moore machine
For a given a state table
  Construct the corresponding state graph

## Slide 4: Moore Machine
The state graph has the output associated with the state
The output is a function of the present state only

## Slide 5: Mealy Machine
The output is a function of the present state and the input
The state graph has the output associated with the arrow

## Slide 6: Construction of State Table and Graphs
Determine the flip-flop input equations and the output equations from the circuit.
Derive the next-state equation for each flip-flop from its input equations, using one of the following relations:
D flip-flop Q+ = D (1)
D-CE flip-flop Q+ = D·CE + Q·CE’ (2)
T-flip-flop Q+ = T XOR Q (3)
S-R flip-flop Q+ = S + R’Q (4)
J-K flip-flop Q+ = JQ’ + K’Q (5)
3. Plot a next-state equations for the flip-flop.
4. Combine these maps to form the state table. Such a state table, which gives the next state of the flip-flops as a function of their present state and the circuit inputs, is frequently referred to as a transition table.
Systematic Approach to Analyze Sequential Circuits

## Slide 7: Construction of State Table and Graphs
Example: To derive the State Table (Moore Machine)
Flip-flop Input equations and Output equation

## Slide 8: Construction of State Table and Graphs
Example: To derive the State Table
1. Determine flip-flop Input equations and Output equations
2. Derive the next-state equation for each flip-flop from its input equation

## Slide 9: Construction of State Table and Graphs
Example: To derive the State Table
2. The next-state equation
3. Karnaugh Maps (Next State Map)

## Slide 10: Construction of State Table and Graphs
AB | A+B+ X = 0 X = 1 | Z
00 01 11 10 | 10 01 00 11 01 11 11 01 | 0 1 0 1
4. To Derive a Transition Table
Present State | Next State |  | Present Output (Z)
 | X = 0 | X = 1 | 
S0 S1 S2 S3 | S3 S0 S1 S2 | S1 S2 S2 S1 | 0 1 0 1

## Slide 11: Construction of State Table and Graphs
5. To Derive a State Graph for Moore Machine
Present State | Next State X = 0 X = 1 | Present Output (Z)
S0 S1 S2 S3 | S3 S1 S0 S2 S1 S2 S2 S1 | 0 1 0 1
state
output
input

## Slide 12: Construction of State Table and Graphs
J-K Flip-Flop (Rising Edge Trigger Type)
J K Q | Q+
0 0 0 0 0 1 0 1 0 0 1 1 1 0 0 1 0 1 1 1 0 1 1 1 | 0 1 0 0 1 1 1 0
Next state table and characteristic equation
Q JK | Q=0 | Q=1
00 | 0 | 1
01 | 0 | 0
11 | 1 | 0
10 | 1 | 1

## Slide 13: Construction of State Table and Graphs
The next-state and output equations are
Example: To derive the State Table (Mealy Machine)

## Slide 14: Construction of State Table and Graphs
The next-state and output maps

## Slide 15: Construction of State Table and Graphs
AB | A+B+ |  | Z | 
 | X=0 | X=1 | X=0 | X=1
00 01 11 10 | 00 01 11 10 | 01 11 00 01 | 0 1 0 0 | 1 0 1 1
Transition Table
Present State | Next State X=0 X=1 | Present Output X=0 X=1
S0 S1 S2 S3 | S0 S1 S1 S2 S2 S0 S3 S1 | 0 1 1 0 0 1 0 1

## Slide 16: Construction of State Table and Graphs
State Graph for Mealy Machine
state
output
input
Present State | Next State X=0 X=1 | Present Output X=0 X=1
S0 S1 S2 S3 | S0 S1 S1 S2 S2 S0 S3 S1 | 0 1 1 0 0 1 0 1

## Slide 18
Part 2 Derivation of State Graphs and Tables

## Slide 19: Objectives
Given a problem statement for the design of a Mealy or Moore sequential circuit,
  find the corresponding state graph and table.
Explain the significance of each state in your graph or table
  in terms of the input sequences required to reach that state.
Check your state graph using appropriate input sequences.

## Slide 20: Design of a Sequence Detector (1)
Sequence Detector to be Designed
X = | 0 | 0 | 1 | 1 | 0 | 1 | 1 | 0 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 0
Z = | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 1 | 0 | 0
(time: | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15)
Z=1 for input sequence of ‘101’

## Slide 21
Mealy Formation of State Graph
Design of a Sequence Detector (1-1)

## Slide 22: Design of a Sequence Detector (1-1)
Mealy State Graph for Sequence Detector

## Slide 23: Design of a Sequence Detector (1-1)
State Table
Transition Table with State Assignment
Present State | Next State |  | Present Output | 
 | X=0 | X=1 | X=0 | X=1
S0 | S0 | S1 | 0 | 0
S1 | S2 | S1 | 0 | 0
S2 | S0 | S1 | 0 | 1
AB | A+B+ |  | Z | 
 | X=0 | X=1 | X=0 | X=1
00 | 00 | 01 | 0 | 0
01 | 10 | 01 | 0 | 0
10 | 00 | 01 | 0 | 1

## Slide 24: Design of a Sequence Detector (1-1)
Map for the Next State
AB | A+B+ |  | Z | 
 | X=0 | X=1 | X=0 | X=1
00 | 00 | 01 | 0 | 0
01 | 10 | 01 | 0 | 0
10 | 00 | 01 | 0 | 1
Map Output Function Z

## Slide 25: Design of a Sequence Detector (1-1)
Final Circuit

## Slide 26: Design of a Sequence Detector (1-2)
Moore Machine Design Process

## Slide 27: Design of a Sequence Detector (1-2)
Moore State Graph for Sequence Detector

## Slide 28: Design of a Sequence Detector (1-2)
State Table
Transition Table with State Assignment
Present State | Next State |  | Present Output (Z)
 | X=0 | X=1 | 
S0 | S0 | S1 | 0
S1 | S2 | S1 | 0
S2 | S0 | S3 | 0
S3 | S2 | S1 | 1
AB | A+B+ |  | Z
 | X=0 | X=1 | 
00 | 00 | 01 | 0
01 | 11 | 01 | 0
11 | 00 | 10 | 0
10 | 11 | 01 | 1

## Slide 29: Design of a Sequence Detector (2)
X= | 0 | 0 | 1 | 0 | 1 | 0 | 0 | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 1 | 1 | 0
 |  |  |  | ↑ |  | ↑ |  | ↑ | ↑ |  |  |  | ↑ |  | ↑ |  | 
 |  |  |  | a |  | b |  | c | d |  |  |  | e |  | f |  | 
Z= | 0 | 0 | 0 | 1 | 0 | 1 | 0 | 1 | 1 | 0 | 0 | 0 | 1 | 0 | 1 | 0 | 0
The circuit to be designed (Mealy)
Output Z=1 if input sequence ends in either 010 or 1001

## Slide 30: Design of a Sequence Detector (2)
Formation of State Graph (010 sequence)
state | sequence received
S0 S1 S2 S3 | reset 0 01 010

## Slide 31: Design of a Sequence Detector (2)
state | sequence ends in
S0 S1 S2 S3 S4 S5 | reset 0 (but not 10) 01 10 1 (but not 01) 100
Formation of State Graph (1001 sequence)

## Slide 32: Design of a Sequence Detector (2)
Completed State Graph for a Sequence Detector to be Designed
state | sequence ends in
S0 S1 S2 S3 S4 S5 | reset 0 (but not 10) 01 10 1 (but not 01) 100

## Slide 33: Design of a Sequence Detector (3)
X= | 1 | 0 | 1 | 1 | 0 | 0 | 1 | 1
 | ↑ |  |  | ↑ |  | ↑ | ↑ | ↑
 | a |  |  | b |  | c | d | e
Z= | (0) | 0 | 0 | 0 | 0 | 1 | 0 | 1
The circuit to be designed (Moore)
Output Z=1 if the total number of 1’s received is odd and at least two consecutive 0’s have been received

## Slide 34: Design of a Sequence Detector (3)
Formation of State Graph (Step 1)

## Slide 35: Design of a Sequence Detector (3)
state | sequence ends in
S0 S1 S2 S3 S4 | reset or even 1’s odd 1’s even 1’s and ends in 0 even 1’s and 00 has occurred 00 has occurred and odd 1’s
Formation of State Graph (Step 2)

## Slide 36: Design of a Sequence Detector (3)
Completed State Graph for a Sequence Detector to be Designed
state | sequence ends in
S0 S1 S2 S3 S4 S5 | reset or even 1’s odd 1’s even 1’s and ends in 0 even 1’s and 00 has occurred odd 1’s and 00 has occurred odd 1’s and ends in 0

## Slide 37: Design of a Sequence Detector (4)
Example: Z=1 when input sequence 0101 or 1001 occurs.
The circuit resets after every four inputs.
Mealy Circuit
X = | 0101 | 0010 | 1001 | 0100
Z = | 0001 | 0000 | 0001 | 0000
A typical sequence of input and output

## Slide 38: Design of a Sequence Detector (4)
Partial State Graph for Example
State | Sequence Received
S0 | reset
S1 | 0
S2 | 1
S3 | 01 or 10
S4 | 010 or 100
The circuit goes to the same state if either 01 or 10 received.

## Slide 39: Design of a Sequence Detector (4)
Complete State Graph for Example
state | sequence received
S0 S1 S2 S3 S4 S5 S6 | reset 0 1 01 or 10 010 or 100 2 inputs received, no 1 output is possible 3 inputs received, no 1 output is possible

## Slide 41
Part 3 Reduction of State Tables State Assignment

## Slide 42: Objectives
Define equivalent states, state several ways of testing for state equivalence, and determine if two states are equivalent.
Define equivalent sequential circuits and determine if two circuits are equivalent.
Reduce a state table to a minimum number of rows.

## Slide 43
Example: Z=1 when input sequence 0101 or 1001 occurs.
The circuit resets after every four inputs.
Mealy Circuit
X = | 0101 | 0010 | 1001 | 0100
Z = | 0001 | 0000 | 0001 | 0000
A typical sequence of input and output
Elimination of Redundant States

## Slide 44
State Table for Sequence Detector (0101, 1001)
Input Sequence | Present State | Next State |  | Present Output | 
 |  | X=0 | X=1 | X=0 | X=1
reset | A | B | C | 0 | 0
0 | B | D | E | 0 | 0
1 | C | F | G | 0 | 0
00 | D | H | I | 0 | 0
01 | E | J | K | 0 | 0
10 | F | L | M | 0 | 0
11 | G | N | P | 0 | 0
000 | H | A | A | 0 | 0
001 | I | A | A | 0 | 0
010 | J | A | A | 0 | 1
011 | K | A | A | 0 | 0
100 | L | A | A | 0 | 1
101 | M | A | A | 0 | 0
110 | N | A | A | 0 | 0
111 | P | A | A | 0 | 0
Elimination of Redundant States

## Slide 45
State Table for Sequence Detector (0101, 1001)
Input Sequence | Present State | Next State |  | Present Output | 
 |  | X=0 | X=1 | X=0 | X=1
reset | A | B | C | 0 | 0
0 | B | D | E | 0 | 0
1 | C | F | G | 0 | 0
00 | D | H | I | 0 | 0
01 | E | J | K | 0 | 0
10 | F | L | M | 0 | 0
11 | G | N | P | 0 | 0
000 | H | A | A | 0 | 0
001 | I | A | A | 0 | 0
010 | J | A | A | 0 | 1
011 | K | A | A | 0 | 0
100 | L | A | A | 0 | 1
101 | M | A | A | 0 | 0
110 | N | A | A | 0 | 0
111 | P | A | A | 0 | 0
Same Next State and Outputs
for the same inputs
H ≡ I
Elimination of Redundant States

## Slide 46
State Table for Sequence Detector (0101, 1001)
Input Sequence | Present State | Next State |  | Present Output | 
 |  | X=0 | X=1 | X=0 | X=1
reset | A | B | C | 0 | 0
0 | B | D | E | 0 | 0
1 | C | F | G | 0 | 0
00 | D | H | I | 0 | 0
01 | E | J | K | 0 | 0
10 | F | L | M | 0 | 0
11 | G | N | P | 0 | 0
000 | H | A | A | 0 | 0
001 | I | A | A | 0 | 0
010 | J | A | A | 0 | 1
011 | K | A | A | 0 | 0
100 | L | A | A | 0 | 1
101 | M | A | A | 0 | 0
110 | N | A | A | 0 | 0
111 | P | A | A | 0 | 0
H ≡ I
Replace I with H
H
Elimination of Redundant States

## Slide 47
State Table for Sequence Detector (0101, 1001)
Input Sequence | Present State | Next State |  | Present Output | 
 |  | X=0 | X=1 | X=0 | X=1
reset | A | B | C | 0 | 0
0 | B | D | E | 0 | 0
1 | C | F | G | 0 | 0
00 | D | H | H | 0 | 0
01 | E | J | K | 0 | 0
10 | F | L | M | 0 | 0
11 | G | N | P | 0 | 0
000 | H | A | A | 0 | 0
010 | J | A | A | 0 | 1
011 | K | A | A | 0 | 0
100 | L | A | A | 0 | 1
101 | M | A | A | 0 | 0
110 | N | A | A | 0 | 0
111 | P | A | A | 0 | 0
Remove I
Elimination of Redundant States

## Slide 48
State Table for Sequence Detector (0101, 1001)
Present State | Next State |  | Present Output | 
 | X=0 | X=1 | X=0 | X=1
A | B | C | 0 | 0
B | D | E | 0 | 0
C | F | G | 0 | 0
D | H | H | 0 | 0
E | J | K | 0 | 0
F | L | M | 0 | 0
G | N | P | 0 | 0
H | A | A | 0 | 0
J | A | A | 0 | 1
K | A | A | 0 | 0
L | A | A | 0 | 1
M | A | A | 0 | 0
N | A | A | 0 | 0
P | A | A | 0 | 0
H ≡ K, M, N, P
Replace K, M, N, P with H
Elimination of Redundant States

## Slide 49
Present State | Next State |  | Present Output | 
 | X=0 | X=1 | X=0 | X=1
A | B | C | 0 | 0
B | D | E | 0 | 0
C | F | G | 0 | 0
D | H | H | 0 | 0
E | J | K H | 0 | 0
F | L | M H | 0 | 0
G | N H | P H | 0 | 0
H | A | A | 0 | 0
J | A | A | 0 | 1
K | A | A | 0 | 0
L | A | A | 0 | 1
M | A | A | 0 | 0
N | A | A | 0 | 0
P | A | A | 0 | 0
State Table for Sequence Detector (0101, 1001)
H ≡ K, M, N, P
Replace K, M, N, P with H
Elimination of Redundant States

## Slide 50
Present State | Next State |  | Present Output | 
 | X=0 | X=1 | X=0 | X=1
A | B | C | 0 | 0
B | D | E | 0 | 0
C | F | G | 0 | 0
D | H | H | 0 | 0
E | J | H | 0 | 0
F | L | H | 0 | 0
G | H | H | 0 | 0
H | A | A | 0 | 0
J | A | A | 0 | 1
L | A | A | 0 | 1
State Table for Sequence Detector (0101, 1001)
Remove K, M, N, P
Elimination of Redundant States

## Slide 51
Present State | Next State |  | Present Output | 
 | X=0 | X=1 | X=0 | X=1
A | B | C | 0 | 0
B | D | E | 0 | 0
C | F | G | 0 | 0
D | H | H | 0 | 0
E | J | H | 0 | 0
F | L | H | 0 | 0
G | H | H | 0 | 0
H | A | A | 0 | 0
J | A | A | 0 | 1
L | A | A | 0 | 1
State Table for Sequence Detector (0101, 1001)
J ≡ L
Replace L with J
Elimination of Redundant States

## Slide 52
Present State | Next State |  | Present Output | 
 | X=0 | X=1 | X=0 | X=1
A | B | C | 0 | 0
B | D | E | 0 | 0
C | F | G | 0 | 0
D | H | H | 0 | 0
E | J | H | 0 | 0
F | L J | H | 0 | 0
G | H | H | 0 | 0
H | A | A | 0 | 0
J | A | A | 0 | 1
L | A | A | 0 | 1
State Table for Sequence Detector (0101, 1001)
J ≡ L
Replace L with J
Elimination of Redundant States

## Slide 53
Present State | Next State |  | Present Output | 
 | X=0 | X=1 | X=0 | X=1
A | B | C | 0 | 0
B | D | E | 0 | 0
C | F | G | 0 | 0
D | H | H | 0 | 0
E | J | H | 0 | 0
F | J | H | 0 | 0
G | H | H | 0 | 0
H | A | A | 0 | 0
J | A | A | 0 | 1
State Table for Sequence Detector (0101, 1001)
Remove L
Elimination of Redundant States

## Slide 54
Present State | Next State |  | Present Output | 
 | X=0 | X=1 | X=0 | X=1
A | B | C | 0 | 0
B | D | E | 0 | 0
C | F | G | 0 | 0
D | H | H | 0 | 0
E | J | H | 0 | 0
F | J | H | 0 | 0
G | H | H | 0 | 0
H | A | A | 0 | 0
J | A | A | 0 | 1
State Table for Sequence Detector (0101, 1001)
D ≡ G
Replace G with D
Elimination of Redundant States

## Slide 55
Present State | Next State |  | Present Output | 
 | X=0 | X=1 | X=0 | X=1
A | B | C | 0 | 0
B | D | E | 0 | 0
C | F | G D | 0 | 0
D | H | H | 0 | 0
E | J | H | 0 | 0
F | J | H | 0 | 0
G | H | H | 0 | 0
H | A | A | 0 | 0
J | A | A | 0 | 1
State Table for Sequence Detector (0101, 1001)
D ≡ G
Replace G with D
Elimination of Redundant States

## Slide 56
Present State | Next State |  | Present Output | 
 | X=0 | X=1 | X=0 | X=1
A | B | C | 0 | 0
B | D | E | 0 | 0
C | F | D | 0 | 0
D | H | H | 0 | 0
E | J | H | 0 | 0
F | J | H | 0 | 0
H | A | A | 0 | 0
J | A | A | 0 | 1
State Table for Sequence Detector (0101, 1001)
E ≡ F
Replace F with E
Elimination of Redundant States

## Slide 57
Present State | Next State |  | Present Output | 
 | X=0 | X=1 | X=0 | X=1
A | B | C | 0 | 0
B | D | E | 0 | 0
C | F E | D | 0 | 0
D | H | H | 0 | 0
E | J | H | 0 | 0
F | J | H | 0 | 0
H | A | A | 0 | 0
J | A | A | 0 | 1
State Table for Sequence Detector (0101, 1001)
E ≡ F
Replace F with E
Elimination of Redundant States

## Slide 58
Present State | Next State |  | Present Output | 
 | X=0 | X=1 | X=0 | X=1
A | B | C | 0 | 0
B | D | E | 0 | 0
C | E | D | 0 | 0
D | H | H | 0 | 0
E | J | H | 0 | 0
H | A | A | 0 | 0
J | A | A | 0 | 1
State Table for Sequence Detector (0101, 1001) (Reduced)
Elimination of Redundant States

## Slide 59
Reduced State Table and Graph for Sequence Detector (0101, 1001)
P.S. | N.S. |  | Output | 
 | X=0 | X=1 | X=0 | X=1
A | B | C | 0 | 0
B | D | E | 0 | 0
C | E | D | 0 | 0
D | H | H | 0 | 0
E | J | H | 0 | 0
H | A | A | 0 | 0
J | A | A | 0 | 1
Row Matching
- Finding equivalent states
Elimination of Redundant States

## Slide 60: Equivalent States
Definition
Let N1 and N2 be sequential circuits (not necessarily different).
Let represent a sequence of inputs of arbitrary length.
Then state in N1 is equivalent to state in N2 iff for every possible input sequence .
are output sequences.
Not practical

## Slide 61: Equivalent States
Theorem
Two states p and q of a sequential circuit are equivalent iff for every single input X, the outputs are the same and the next states are equivalent, that is,
Equivalent
are output sequences.
are next state sequences.

## Slide 62: Determination of State Equivalence Using an Implication Table
Example: Table 9-1
Implication Chart for Table 9-1
Present State | Next State |  | Present Output
 | X=0 | X=1 | 
a | d | c | 0
b | f | h | 0
c | e | d | 1
d | a | e | 0
e | c | a | 1
f | f | b | 1
g | b | h | 0
h | c | g | 1
b | d-f c-h |  |  |  |  |  | 
c |  |  |  |  |  |  | 
d | a-d c-e | a-f e-h |  |  |  |  | 
e |  |  | c-e a-d |  |  |  | 
f |  |  | e-f b-d |  | c-f a-b |  | 
g | b-d c-h | b-f |  | a-b e-h |  |  | 
h |  |  | c-e d-g |  | a-g | c-f b-g | 
 | a | b | c | d | e | f | g

## Slide 63: Determination of State Equivalence Using an Implication Table
Present State | Next State |  | Present Output
 | X=0 | X=1 | 
a | d | c | 0
b | f | h | 0
c | e | d | 1
d | a | e | 0
e | c | a | 1
f | f | b | 1
g | b | h | 0
h | c | g | 1
b | d-f c-h |  |  |  |  |  | 
c |  |  |  |  |  |  | 
d | a-d c-e | a-f e-h |  |  |  |  | 
e |  |  | c-e a-d |  |  |  | 
f |  |  | e-f b-d |  | c-f a-b |  | 
g | b-d c-h | b-f |  | a-b e-h |  |  | 
h |  |  | c-e d-g |  | a-g | c-f b-g | 
 | a | b | c | d | e | f | g
Remove Self-implied
Example: Table 9-1
Implication Chart for Table 9-1

## Slide 64: Determination of State Equivalence Using an Implication Table
Present State | Next State |  | Present Output
 | X=0 | X=1 | 
a | d | c | 0
b | f | h | 0
c | e | d | 1
d | a | e | 0
e | c | a | 1
f | f | b | 1
g | b | h | 0
h | c | g | 1
b | d-f c-h |  |  |  |  |  | 
c |  |  |  |  |  |  | 
d | c-e | a-f e-h |  |  |  |  | 
e |  |  | a-d |  |  |  | 
f |  |  | e-f b-d |  | c-f a-b |  | 
g | b-d c-h | b-f |  | a-b e-h |  |  | 
h |  |  | c-e d-g |  | a-g | c-f b-g | 
 | a | b | c | d | e | f | g
After removing Self-implied
Example: Table 9-1
Implication Chart for Table 9-1

## Slide 65: Determination of State Equivalence Using an Implication Table
Present State | Next State |  | Present Output
 | X=0 | X=1 | 
a | d | c | 0
b | f | h | 0
c | e | d | 1
d | a | e | 0
e | c | a | 1
f | f | b | 1
g | b | h | 0
h | c | g | 1
b | d-f c-h |  |  |  |  |  | 
c |  |  |  |  |  |  | 
d | c-e | a-f e-h |  |  |  |  | 
e |  |  | a-d |  |  |  | 
f |  |  | e-f b-d |  | c-f a-b |  | 
g | b-d c-h | b-f |  | a-b e-h |  |  | 
h |  |  | c-e d-g |  | a-g | c-f b-g | 
 | a | b | c | d | e | f | g
Remove non-equivalent pairs
Example: Table 9-1
Implication Chart for Table 9-1

## Slide 66: Determination of State Equivalence Using an Implication Table
Present State | Next State |  | Present Output
 | X=0 | X=1 | 
a | d | c | 0
b | f | h | 0
c | e | d | 1
d | a | e | 0
e | c | a | 1
f | f | b | 1
g | b | h | 0
h | c | g | 1
b | d-f c-h |  |  |  |  |  | 
c |  |  |  |  |  |  | 
d | c-e | a-f e-h |  |  |  |  | 
e |  |  | a-d |  |  |  | 
f |  |  | e-f b-d |  | c-f a-b |  | 
g | b-d c-h | b-f |  | a-b e-h |  |  | 
h |  |  | c-e d-g |  | a-g | c-f b-g | 
 | a | b | c | d | e | f | g
Remove non-equivalent pairs
Example: Table 9-1
Implication Chart for Table 9-1

## Slide 67: Determination of State Equivalence Using an Implication Table
Present State | Next State |  | Present Output
 | X=0 | X=1 | 
a | d | c | 0
b | f | h | 0
c | e | d | 1
d | a | e | 0
e | c | a | 1
f | f | b | 1
g | b | h | 0
h | c | g | 1
b | d-f c-h |  |  |  |  |  | 
c |  |  |  |  |  |  | 
d | c-e | a-f e-h |  |  |  |  | 
e |  |  | a-d |  |  |  | 
f |  |  | e-f b-d |  | c-f a-b |  | 
g | b-d c-h | b-f |  | a-b e-h |  |  | 
h |  |  | c-e d-g |  | a-g | c-f b-g | 
 | a | b | c | d | e | f | g
Remove non-equivalent pairs
Example: Table 9-1
Implication Chart for Table 9-1

## Slide 68: Determination of State Equivalence Using an Implication Table
Present State | Next State |  | Present Output
 | X=0 | X=1 | 
a | d | c | 0
b | f | h | 0
c | e | d | 1
d | a | e | 0
e | c | a | 1
f | f | b | 1
g | b | h | 0
h | c | g | 1
b | d-f c-h |  |  |  |  |  | 
c |  |  |  |  |  |  | 
d | c-e | a-f e-h |  |  |  |  | 
e |  |  | a-d |  |  |  | 
f |  |  | e-f b-d |  | c-f a-b |  | 
g | b-d c-h | b-f |  | a-b e-h |  |  | 
h |  |  | c-e d-g |  | a-g | c-f b-g | 
 | a | b | c | d | e | f | g
Remove non-equivalent pairs
Example: Table 9-1
Implication Chart for Table 9-1

## Slide 69: Determination of State Equivalence Using an Implication Table
Present State | Next State |  | Present Output
 | X=0 | X=1 | 
a | d | c | 0
b | f | h | 0
c | e | d | 1
d | a | e | 0
e | c | a | 1
f | f | b | 1
g | b | h | 0
h | c | g | 1
b | d-f c-h |  |  |  |  |  | 
c |  |  |  |  |  |  | 
d | c-e | a-f e-h |  |  |  |  | 
e |  |  | a-d |  |  |  | 
f |  |  | e-f b-d |  | c-f a-b |  | 
g | b-d c-h | b-f |  | a-b e-h |  |  | 
h |  |  | c-e d-g |  | a-g | c-f b-g | 
 | a | b | c | d | e | f | g
Remove non-equivalent pairs
Example: Table 9-1
Implication Chart for Table 9-1

## Slide 70: Determination of State Equivalence Using an Implication Table
Present State | Next State |  | Present Output
 | X=0 | X=1 | 
a | d | c | 0
b | f | h | 0
c | e | d | 1
d | a | e | 0
e | c | a | 1
f | f | b | 1
g | b | h | 0
h | c | g | 1
b | d-f c-h |  |  |  |  |  | 
c |  |  |  |  |  |  | 
d | c-e | a-f e-h |  |  |  |  | 
e |  |  | a-d |  |  |  | 
f |  |  | e-f b-d |  | c-f a-b |  | 
g | b-d c-h | b-f |  | a-b e-h |  |  | 
h |  |  | c-e d-g |  | a-g | c-f b-g | 
 | a | b | c | d | e | f | g
Remove non-equivalent pairs
Example: Table 9-1
Implication Chart for Table 9-1

## Slide 71: Determination of State Equivalence Using an Implication Table
Present State | Next State |  | Present Output
 | X=0 | X=1 | 
a | d | c | 0
b | f | h | 0
c | e | d | 1
d | a | e | 0
e | c | a | 1
f | f | b | 1
g | b | h | 0
h | c | g | 1
b | d-f c-h |  |  |  |  |  | 
c |  |  |  |  |  |  | 
d | c-e | a-f e-h |  |  |  |  | 
e |  |  | a-d |  |  |  | 
f |  |  | e-f b-d |  | c-f a-b |  | 
g | b-d c-h | b-f |  | a-b e-h |  |  | 
h |  |  | c-e d-g |  | a-g | c-f b-g | 
 | a | b | c | d | e | f | g
Remove non-equivalent pairs
Example: Table 9-1
Implication Chart for Table 9-1

## Slide 72: Determination of State Equivalence Using an Implication Table
Present State | Next State |  | Present Output
 | X=0 | X=1 | 
a | d | c | 0
b | f | h | 0
c | e | d | 1
d | a | e | 0
e | c | a | 1
f | f | b | 1
g | b | h | 0
h | c | g | 1
b | d-f c-h |  |  |  |  |  | 
c |  |  |  |  |  |  | 
d | c-e | a-f e-h |  |  |  |  | 
e |  |  | a-d |  |  |  | 
f |  |  | e-f b-d |  | c-f a-b |  | 
g | b-d c-h | b-f |  | a-b e-h |  |  | 
h |  |  | c-e d-g |  | a-g | c-f b-g | 
 | a | b | c | d | e | f | g
After first pass
Example: Table 9-1
Implication Chart for Table 9-1

## Slide 73: Determination of State Equivalence Using an Implication Table
Present State | Next State |  | Present Output
 | X=0 | X=1 | 
a | d | c | 0
b | f | h | 0
c | e | d | 1
d | a | e | 0
e | c | a | 1
f | f | b | 1
g | b | h | 0
h | c | g | 1
b | d-f c-h |  |  |  |  |  | 
c |  |  |  |  |  |  | 
d | c-e | a-f e-h |  |  |  |  | 
e |  |  | a-d |  |  |  | 
f |  |  | e-f b-d |  | c-f a-b |  | 
g | b-d c-h | b-f |  | a-b e-h |  |  | 
h |  |  | c-e d-g |  | a-g | c-f b-g | 
 | a | b | c | d | e | f | g
Remove non-equivalent pairs
Example: Table 9-1
Implication Chart for Table 9-1

## Slide 74: Determination of State Equivalence Using an Implication Table
Present State | Next State |  | Present Output
 | X=0 | X=1 | 
a | d | c | 0
b | f | h | 0
c | e | d | 1
d | a | e | 0
e | c | a | 1
f | f | b | 1
g | b | h | 0
h | c | g | 1
b | d-f c-h |  |  |  |  |  | 
c |  |  |  |  |  |  | 
d | c-e | a-f e-h |  |  |  |  | 
e |  |  | a-d |  |  |  | 
f |  |  | e-f b-d |  | c-f a-b |  | 
g | b-d c-h | b-f |  | a-b e-h |  |  | 
h |  |  | c-e d-g |  | a-g | c-f b-g | 
 | a | b | c | d | e | f | g
Remove non-equivalent pairs
Example: Table 9-1
Implication Chart for Table 9-1

## Slide 75: Determination of State Equivalence Using an Implication Table
Present State | Next State |  | Present Output
 | X=0 | X=1 | 
a | d | c | 0
b | f | h | 0
c | e | d | 1
d | a | e | 0
e | c | a | 1
f | f | b | 1
g | b | h | 0
h | c | g | 1
b | d-f c-h |  |  |  |  |  | 
c |  |  |  |  |  |  | 
d | c-e | a-f e-h |  |  |  |  | 
e |  |  | a-d |  |  |  | 
f |  |  | e-f b-d |  | c-f a-b |  | 
g | b-d c-h | b-f |  | a-b e-h |  |  | 
h |  |  | c-e d-g |  | a-g | c-f b-g | 
 | a | b | c | d | e | f | g
Remove non-equivalent pairs
Example: Table 9-1
Implication Chart for Table 9-1

## Slide 76: Determination of State Equivalence Using an Implication Table
Present State | Next State |  | Present Output
 | X=0 | X=1 | 
a | d | c | 0
b | f | h | 0
c | e | d | 1
d | a | e | 0
e | c | a | 1
f | f | b | 1
g | b | h | 0
h | c | g | 1
b | d-f c-h |  |  |  |  |  | 
c |  |  |  |  |  |  | 
d | c-e | a-f e-h |  |  |  |  | 
e |  |  | a-d |  |  |  | 
f |  |  | e-f b-d |  | c-f a-b |  | 
g | b-d c-h | b-f |  | a-b e-h |  |  | 
h |  |  | c-e d-g |  | a-g | c-f b-g | 
 | a | b | c | d | e | f | g
After second pass
Example: Table 9-1
Implication Chart for Table 9-1

## Slide 77: Determination of State Equivalence Using an Implication Table
Implication Chart After Second Pass
b | d-f c-h |  |  |  |  |  | 
c |  |  |  |  |  |  | 
d | c-e | a-f e-h |  |  |  |  | 
e |  |  | a-d |  |  |  | 
f |  |  | e-f b-d |  | c-f a-b |  | 
g | b-d c-h | b-f |  | a-b e-h |  |  | 
h |  |  | c-e d-g |  | a-g | c-f b-g | 
 | a | b | c | d | e | f | g
Present State | Next State |  | Present Output
 | X=0 | X=1 | 
a | d | c | 0
b | f | h | 0
c | e c | d | 1
d | a | e c | 0
e | c | a | 1
f | f | b | 1
g | b | h | 0
h | c | g | 1
Replace e with c

## Slide 78: Determination of State Equivalence Using an Implication Table
Implication Chart After Second Pass
b | d-f c-h |  |  |  |  |  | 
c |  |  |  |  |  |  | 
d | c-e | a-f e-h |  |  |  |  | 
e |  |  | a-d |  |  |  | 
f |  |  | e-f b-d |  | c-f a-b |  | 
g | b-d c-h | b-f |  | a-b e-h |  |  | 
h |  |  | c-e d-g |  | a-g | c-f b-g | 
 | a | b | c | d | e | f | g
Present State | Next State |  | Present Output
 | X=0 | X=1 | 
a | d a | c | 0
b | f | h | 0
c | c | d a | 1
d | a | c | 0
f | f | b | 1
g | b | h | 0
h | c | g | 1
Replace d with a

## Slide 79: Determination of State Equivalence Using an Implication Table
Present State | Next State |  | Present Output
 | X=0 | X=1 | 
a | a | c | 0
b | f | h | 0
c | c | a | 1
f | f | b | 1
g | b | h | 0
h | c | g | 1
State table after reduction
Present State | Next State |  | Present Output
 | X=0 | X=1 | 
a | d | c | 0
b | f | h | 0
c | e | d | 1
d | a | e | 0
e | c | a | 1
f | f | b | 1
g | b | h | 0
h | c | g | 1
State table before reduction